## Slide 1: Unit-2: Wireless Communication Technology PART-3 : Spread Spectrum
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof.Swati R Sharma
Mobile Computing Wireless Communication
(MCWC)
GTU # 3170710

## Slide 2: Spread Spectrum

Looping
Topics to be covered- Spread Spectrum
  The Concept of Spread Spectrum
  Frequency Hopping Spread Spectrum
  Direct Sequence Spread Spectrum
  Code Division Multiple Access

## Slide 3: The Concept of Spread Spectrum

## Slide 4: The Concept of Spread Spectrum
A collective class of signalling techniques are employed before transmitting a signal to provide a secure communication, known as the Spread Spectrum Modulation.
The pivotal aim of spread spectrum communication technique is to prevent “interference” whether it is intentional or unintentional.’
The spread spectrum signals are hard to interfere and can’t be jammed.

## Slide 5: The Concept of Spread Spectrum
Narrow Band Signal features
  Band of signals occupy a narrow range of frequencies
  Power density is high
  Spread of energy is low and concentrated
  Signals are prone to interference
Spread Spectrum Signal features
  Band of signals occupy a wide range of frequencies
  Power density is very low
  Energy is wide spread
  Highly resistant to interference or jamming

## Slide 6: General model of Spread Spectrum
Channel Encoder
Channel Decoder
Modulator
Demodulator
Channel
Psuedo-noise generator
Psuedo-noise generator
Input
Data
Output
Data
Spreading
Code
Spreading
Code

## Slide 7: The Concept of Spread Spectrum
Applications
  Military communication
  It can also be used for hiding and encrypting signals. Only a recipient who knows the spreading code can recover the encoded information.

## Slide 8: Spread Spectrum Technique
Spread Spectrum
Frequency Hoping Spread Spectrum
(FHSS)
Direct Sequence
Spread Spectrum
(DSSS)

## Slide 9: Frequency Hopping Spread Spectrum(FHSS)

## Slide 10: Frequency Hopping Spread Spectrum(FHSS)
The first type of spread spectrum developed is known as frequency hopping.
The sequence of channels used is indicated by a spreading code.
Signal is broadcast over seemingly random series of radio frequencies
  A number of channels allocated for the FH signal
  Width of each channel corresponds to bandwidth of input signal
Signal hops from frequency to frequency at fixed intervals
  Transmitter operates in one channel at a time
  Bits are transmitted using some encoding scheme
  At each successive interval, a new carrier frequency is selected

## Slide 11: FHSS Transmitter and Receiver block diagram
FHSS Transmitter
FHSS Receiver

## Slide 12: Direct Sequence Spread Spectrum(DSSS)

## Slide 13: Direct Sequence Spread Spectrum(DSSS)
Each bit in original signal is represented by multiple bits in the transmitted signal
Spreading code spreads signal across a wider frequency band
Spread is in direct proportion to number of bits used
One technique combines digital information stream with the spreading code bit stream using exclusive-OR.

## Slide 14: Direct Sequence Spread Spectrum
0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0
0
1
Data Input Signal (A)
PN bit stream (B)
C=A ⊕ B
0
0
1
1
0
1

## Slide 15: DSSS Transmitter and Receiver block diagram
DSSS Transmitter
DSSS Receiver

## Slide 16: DSSS Performance Considerations

## Slide 17: Code Division Multiple Access
CDMA is a multiplexing technique used with spread spectrum.

## Slide 18: Code Division Multiple Access :Example
 | User-1 | User-2 | User-3
Data | 00 | 10 | 11
Spread Code | 0101 | 0011 | 0000
Generated Spread code |  |  | 
00
:0000 0000
⊕:0101 0101
0101
0101 0101
10: 1111 0000
0011: ⊕0011 0011
1100 0011
11: 1111 1111
0000: ⊕ 0000 0000
1111 1111

## Slide 19
Spread code |  |  | 
0101 0101
1100 0011
1111 1111
CDMA | User-1 | User-2 | User-3
User-1 |  |  |  |  |  |  |  |  | 
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0: +1V
1: -1V
0V
+1V
-1V
User-2 |  |  |  |  |  |  |  |  | 
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0V
+1V
-1V
User-3 |  |  |  |  |  |  |  |  | 
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0V
+1V
-1V

## Slide 20
User-1 |  |  |  |  |  |  |  |  | 
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0: +1V
1: -1V
0V
+1V
-1V
User-2 |  |  |  |  |  |  |  |  | 
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0V
+1V
-1V
User-3 |  |  |  |  |  |  |  |  | 
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0V
+1V
-1V
+1 | -1 | +1 | -1 | +1 | -1 | +1 | -1
-1 | -1 | +1 | +1 | +1 | +1 | -1 | -1
-1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
Receiver

## Slide 21
User-1 | Volts |  |  |  |  |  |  |  | 
User-2 | Volts |  |  |  |  |  |  |  | 
User-3 | Volts |  |  |  |  |  |  |  | 
+1 | -1 | +1 | -1 | +1 | -1 | +1 | -1
-1 | -1 | +1 | +1 | +1 | +1 | -1 | -1
-1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
Composite Signal(Add) |  |  |  |  |  |  |  |  | 
+1V
0V
-1V
-2V
-3V
Composite Signal(Add) | Volts | -1 | -3 | 1 | -1 | 1 | -1 | -1 | -3
CDMA Transmitter

## Slide 22
Composite Signal(Add) |  |  |  |  |  |  |  |  | 
+1V
0V
-1V
-2V
-3V
User1(0101) |  |  |  |  |  |  |  |  | 
0: +1V
1: -1V
0V
-1V
+1V
Multiply | Volts | -1 | 3 | 1 | 1 | 1 | 1 | -1 | 3
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
-1+3+1+1=4/4=+1
+1+1-1+3=4/4=+1
Voltage=11
Therefore, Data=00(i.e Original Data Sent by User-1)
0: +1V
1: -1V
CDMA Receiver
USER-1

## Slide 23
Composite Signal(Add) |  | -1 | -3 | 1 | -1 | 1 | -1 | -1 | -3
+1V
0V
-1V
-2V
-3V
User2(0011) |  |  |  |  |  |  |  |  | 
0: +1V
1: -1V
0V
-1V
+1V
Multiply | Volts | -1 | -3 | -1 | 1 | 1 | -1 | 1 | 3
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
-1-3-1+1=-4/4=-1
+1-1+1+3=4/4=+1
Voltage= -1 1
Therefore, Data=10(i.e Original Data Sent by User-2)
0: +1V
1: -1V
CDMA Receiver
USER-2
+1 | +1 | -1 | -1 | +1 | +1 | -1 | -1

## Slide 24
Composite Signal(Add) |  | -1 | -3 | 1 | -1 | 1 | -1 | -1 | -3
+1V
0V
-1V
-2V
-3V
User3(0000) |  |  |  |  |  |  |  |  | 
0: +1V
1: -1V
0V
-1V
+1V
Multiply | Volts | -1 | -3 | 1 | -1 | 1 | -1 | -1 | -3
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-1-3+1-1=-4/4=-1
+1-1-1-3=-4/4=-1
Voltage= -1 -1
Therefore, Data=11(i.e Original Data Sent by User-3)
0: +1V
1: -1V
CDMA Receiver
USER-3
+1 | +1 | +1 | +1 | +1 | +1 | +1 | +1

## Slide 25: GTU Questions: Unit 2-Part 3
Sr. | Question | Marks | Year
1. | What is Direct Sequence Spread Spectrum technology? How does it work in CDMA technology? | 7 3 | Win’18 Sum’20
2. | What is wave propagation? Discuss various modes of propagation with example | 4 7 7 | Sum’19 Win’19 Sum’20
3. | Explain FHSS. Discuss advantages and applications of FHSS. | 7 4 7 | Sum’19 Win’19 Sum’20
4. | How DSSS does works in CDMA technology? | 4 | Sum’20

## Slide 26: References
Book: | Wireless Communications & Networks, Second Edition, William Stallings by Pearson

## Slide 27: Thank You