## Slide 1: Introduction to MCWC
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof.Swati R Sharma
Mobile Computing Wireless Communication
(MCWC)
GTU # 3170710

## Slide 2: MCWC GTU Syllabus
Unit | Unit Name
1 | Introduction to Transmission Fundamentals and Communication
2 | Wireless Communication Technology-Cellular Wireless Networks, Antennas and Propagation, Spread Spectrum, Coding and Error Control
3 | Multiple access in Wireless System including GSM, GPRS, WiMax and Mobile IP
4 | Wi-Fi and the IEEE 802.11 Wireless LAN Standard
5 | Bluetooth
6 | Android Programming

## Slide 3: Reference Books
Unit | Reference Books
1 | Wireless Communications & Networks, Second Edition, William Stallings by Pearson
2 | 
3 | Wireless Communications & Networks, Second Edition, William Stallings by Pearson
 | Mobile Computing Technology, Applications and service creation, Asoke K Telukder, Roopa R Yavagal by TMH
4 | Wireless Communications & Networks, Second Edition, William Stallings by Pearson
5 | 
6 | Android Application Development Black Book, Pradeep Kothari, dreamtech press.

## Slide 4: Unit-1: Introduction to Transmission Fundamentals
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof.Swati R Sharma
Mobile Computing Wireless Communication
(MCWC)
GTU # 3170710

## Slide 5: What is MCWC (Mobile Computing and Wireless Communication)?
Mobile Computing
“Mobile Computing is a technology that allows transmission of
data,
voice and
video
via a computer or any other wireless enabled device without having to be connected to a fixed physical link.”

## Slide 6: Why MCWC Subject?
University had enrolled this subject (MCWC) for the students to make them understand:
  Mobile and wireless network systems such as 2G/3G/4G mobile telephony/data networks
  Understand GSM , GPRS , MobileIP
  Understand the working of wireless local area network, Bluetooth.
  Basics Mobile App Development using Android

## Slide 7: Transmission Fundamentals

Looping
Topics to be covered
  Signals for Conveying Information
  Time Domain Concept
  Frequency Domain Concept
  Relationship between Data Rate and Bandwidth
  Analog and Digital Data Transmission
  Reasons for Choosing Data and Signal Combinations
  Channel Capacity
  Transmission Media
  Multiplexing

## Slide 8: Signals for Conveying Information
Electromagnetic Signals:
The signals which are used as means to transmit information are known as Electromagnetic Signals.
It can be expressed as:
  Function of Time
  Function of Frequency

## Slide 9: Time Domain Concept

## Slide 10: Time Domain Concept
Analog Signal
Signal intensity varies in a smooth fashion over time
  No breaks or discontinuities in the signal
  Application: audio and video transmission.
  Example: Temperature sensors, FM radio, Photocells, Light sensor etc.
Digital Signal
Signal intensity maintains a constant level for some period of time and then changes to another constant level
  Application: Computing and digital electronics
  Example: Computers, CDs, DVDs

## Slide 11: Time Domain Concept
Periodic signal
An analog or digital signal pattern that repeats over time.
Aperiodic signal
An analog or digital signal pattern that doesn't repeat over time.
Equation: s(t) = s(t+T),-∞<t<+∞
where T is the period of the signal

## Slide 12: Time Domain Concept
Peak amplitude (A):
  Maximum value or strength of the signal over time
  Typically measured in volts
Frequency (f):
  Rate, in cycles per second, or Hertz (Hz), at which the signal repeats.
Phase ():
  A measurement of the relative position in time within a single period of a signal.
Wavelength ():
  A distance occupied by a single cycle of the signal.
  Or, the distance between two points of corresponding phase of two consecutive cycles

## Slide 13: Frequency Domain Concept

## Slide 14: Frequency Domain Concept
Fundamental frequency: when all frequency components of a signal are integer multiples of one frequency, it’s referred to as the fundamental frequency
  The period of the total signal is equal to the period of the fundamental frequency
Spectrum - Range of frequencies that a signal contains
Absolute bandwidth - Width of the spectrum of a signal
Effective bandwidth (or just bandwidth) - Narrow band of frequencies that most of the signal’s energy is contained in

## Slide 15: Relationship between Data Rate and Bandwidth

## Slide 16: Relationship between Data Rate and Bandwidth
The greater the bandwidth, the higher the information-carrying capacity
Conclusions
  Any digital waveform will have infinite bandwidth
  BUT the transmission system will limit the bandwidth that can be transmitted
  AND, for any given medium, the greater the bandwidth transmitted, the greater the cost
  HOWEVER, limiting the bandwidth creates distortions

## Slide 17: Analog and Digital Data Transmission

## Slide 18: Analog and Digital Data Transmission
Data Communication Terms
Data as entities that convey meaning, or information.
Signals are electric or electromagnetic representations of data.
Transmission is the communication of data by the propagation and processing of signals.

## Slide 19: Analog vs Digital Transmission
Analog Transmission | Digital Transmission
Analog signal is a continuous signal which represents physical measurements. | Digital signals are discrete time signals generated by digital modulation.
Represented by sine waves | Represented by square waves
Uses continuous range of values to represent information | Uses discrete or discontinuous values to represent information
Stored in the form of wave signal | Stored in the form of binary bit
Analog instrument draws large power | Digital instrument draws only negligible power
Can be used in analog device only. Best suited for audio and video transmission. | Best suited for Computing and digital electronics.
Subjected to deterioration by noise during transmission | Can be noise-immune without deterioration during transmission

## Slide 20: Analog and Digital Transmission Example

## Slide 21: Reasons for Choosing Data and Signal Combinations

## Slide 22: Reasons for Choosing Data and Signal Combinations

## Slide 23: Channel Capacity

## Slide 24: Channel Capacity
Channel Capacity: The maximum rate at which data can be transmitted over a given communication path, or channel, under given conditions.
Data rate: Rate at which data can be communicated (bps).
  Data rate is the speed at which data is transferred between two devices, measured in mega bits per second (Mbps or mbps)
Bandwidth: The bandwidth of the transmitted signal as constrained by the transmitter and the nature of the transmission medium (Hertz)
  Bandwidth is measured as the amount of data that can be transferred from one point to another within a network in a specific amount of time.
Noise: Average level of disturbance over the communications path
  noise is an unwanted disturbance in an electrical signal
Error rate - rate at which errors occur
  Error = transmit 1 and receive 0; transmit 0 and receive 1

## Slide 25: Bandwidth Comparison
Generation | Technology | Maximum Download Speed
2G | GPRS-Global Positioning Radio System, EDGE-Enhanced Data Rates for GSM Evolution | 64Kbps
3G | HSPA-High Speed Packet Access DCHSPA-Dual Access HSPA | 2Mbps
4G | LTE-Long Term Evolution | 2000Mbps to 1Gbps
5G | 5G | 1Gbps & higher

## Slide 26: Transmission Impairment

## Slide 27: Transmission Impairment
Impairment causes
Attenuation
Distortion
Noise

## Slide 28: What is Noise?
Noise: The random/unwanted signal that mixes with the original signal is known as noise.
Types of Noise:
  Induced noise: Noise from sources such as motors and appliances.
  Crosstalk noise: Noise generates when one wire affects the other wire.
  Thermal noise: Noise from movement of electrons in wire which creates an extra signal
  Impulse noise: Signal with high energy that comes from lightning or power lines

## Slide 29: What is Distortion?
Change in the shape of signal.
Generally observed in composite signals with different frequencies.
Each frequency component has its own propagation speed travelling through a medium.
Every component arrive at different time which leads to delay distortion.

## Slide 30: What is Attenuation?
Loss of energy.
The strength of signal decreases with increasing distance which causes loss of energy in overcoming resistance of medium.
Amplifiers are used to amplify the attenuated signal which gives the original signal back.

## Slide 31: Maximum Data Rate for Noiseless and Noisy channels

## Slide 32: Maximum Data Rate for Noiseless and Noisy channels
Data rate: Rate at which data can be communicated (bps).
  Data rate is the speed at which data is transferred between two devices, measured in mega bits per second (Mbps or mbps)
Data rate depends upon 3 factors:
  Bandwidth available
  Number of levels in digital signal
  The quality of the channel i.e. level of noise
To calculate data rate 2 theoretical formulas were developed:
  Nyquist Bandwidth-> noiseless channel
  Shannon Capacity Formula-> noisy channel

## Slide 33: Nyquist Bandwidth for noiseless channel

## Slide 34: Nyquist Bandwidth for noiseless channel
Nyquist Bandwidth is relationship between bandwidth and its information carrying capacity.
Nyquist's theorem specifies the maximum data rate for noiseless condition.
Nyquist's theorem states that if the rate of signal transmission is 2B(Bandwidth), then a signal with frequency no greater than B is sufficient to carry the signal rate.
There are two types of signal:
  Binary Signals (Two level: 0 and 1)
  Multilevel Signals (More than two level)

## Slide 35: Nyquist Bandwidth for noiseless channel
Nyquist formula for maximum bitrate in bits per second(bps) for noiseless channel.
For binary signals (two voltage levels)
            C: Channel Capacity
            B: Bandwidth
  For multilevel signaling (more than two voltage levels)
    M:Number of discrete signal or voltage levels
            C: Channel Capacity
            B: Bandwidth
Binary Signal
Multilevel Signal
  C = 2B
  C = 2B log2 M

## Slide 36: Nyquist Bandwidth: Example
Given: B=3100 Hz
Formula for binary signal: C = 2B
C = 2 X 3100
Answer: C = 6200 bps(bits per second)
Therefore, channel capacity C is 6200 bps(bits per second) if bandwidth B is 3100Hz.
Example 1: | If the signal transmitted is binary and bandwidth is 3100 Hz then calculate the channel capacity.
Solution 1:

## Slide 37: Nyquist Bandwidth: Example
Given: Bandwidth B=3100 Hz
Signal Level M=8
Formula for Multilevel signal: C = 2B log2 M
C = 2 X 3100 X log2 8 (log2 8 = 3)
C = 2 X 3100 X 3
Answer: C = 18,600 bps(bits per second)
Conclusion:
Therefore, for a given bandwidth, the data rate can be increased by increasing the number of different signal elements(M).
Nyquist's formula indicates that, doubling the bandwidth doubles data rate.
Example 2: | If the signal transmitted is multilevel and bandwidth is 3100 Hz with 8 possible voltage/signal levels are used then calculate the channel capacity.
Solution 2:

## Slide 38: Signal-to-Noise Ratio

## Slide 39: Signal-to-Noise Ratio
Ratio of the power in a signal to the power contained in the noise that’s present at a particular point in the transmission
Typically measured at a receiver end
Signal-to-noise ratio (SNR, or S/N)
A high SNR means a high-quality signal, low number of required intermediate repeaters
SNR sets upper bound on achievable data rate.
A high SNR, means a high-quality signal.

## Slide 40: Shannon Capacity Formula for noisy channel

## Slide 41: Shannon Capacity Formula for noisy channel
In real, we cannot have a noiseless channel; the channel is always noisy.
Shannon capacity specifies the theoretical highest data rate for a noisy channel.
Shannon Capacity Formula:
            C: Channel Capacity(bps)
            B: Bandwidth(Hz)
In practice, only much lower rates achieved
  Formula assumes white noise (thermal noise)
  Impulse noise is not accounted for
  Attenuation distortion or delay distortion not accounted for

## Slide 42: Nyquist and Shannon Formulations

## Slide 43: Nyquist and Shannon Formulations
Given: Bandwidth B=4MHz–3MHz=1MHz
SNR=24dB=10log10(SNR)=251
Using Shannon’s formula
C = B * log2(1+SNR)
= 1MHz * log2(1+251)
= 106 * log2(1+251)
≈ 106 * 8
C = 8Mbps
Example1: | The spectrum of channel is between 3MHz and 4MHz and SNR is 24DB. Find out channel capacity using Shannon formula.
Note:
SNRdB = 10 log10(SNR)
when stated in dB, so be careful about mixing the two logarithmic bases in this problem.
The SNR quantity in the Shannon capacity equation is numerical (not dB) and the logarithm is base 2.
SNR of 24dB is numerically equal to 251
SNRdB = 24dB = 10log10(SNR)
24=10log10(SNR)
2.4=log10(SNR)
SNR=102.4= 251
Solution:
logbx=y by=x

## Slide 44: Nyquist and Shannon Formulations
Given: Bandwidth B = 1MHz
SNR = 63
Find: Bit rate C
Using Shannon’s formula
C = B * log2(1+SNR)
= 1MHz * log2(1+63)
= 106 * log2(1+63)
≈ 106 * 6
C = 6Mbps
Example2: | We have a channel with 1-MHz bandwidth. The SNR =63. What are the appropriate Bit rate and Signal level using Shannon’s and Nyquist’s Formula? [GTU Winter 2019]
Find: Signal level M, if C=6Mbps
Using Nyquist’s Formula
C = 2B * log2M
6Mbps = 2 * 1MHz * log2M
6*106 = 2*(1*106) * log2M
3 = log2M
M = 23
M = 8
Solution:
Solution:

## Slide 45: Nyquist and Shannon Formulations
Example3: | A typical voice channel has SNR as 30dB and Bandwidth as 2.7KHz. Calculate the approximate maximum information capacity of the channel? [GTU Winter 2019]
Given: Bandwidth B=2.7KHz
SNR=30dB=10log10(SNR)=1000
Using Shannon’s formula
C = B * log2(1+SNR)
= 2.7KHz * log2(1+1000)
= (2.7*103) * log2(1+1000)
= 2700 * 9.967 = 26910.99
≈ 27000
C ≈ 27Kbps
Note:
SNRdB = 10 log10(SNR)
when stated in dB, so be careful about mixing the two logarithmic bases in this problem.
The SNR quantity in the Shannon capacity equation is numerical (not dB) and the logarithm is base 2.
SNR of 30dB is numerically equal to 1000
SNRdB = 30dB = 10log10(SNR)
30=10log10(SNR)
3=log10(SNR)
SNR =103= 1000
Solution:

## Slide 46: Exercise
1. | If the SNR of wireless channel 10dB then calculate maximum data rate through channel with bandwidth of 200 KHz. Answer[691.8 kbps]
Given: Bandwidth B=200KHz
SNR=10dB=10log10(SNR)=10
Using Shannon’s formula
C = B * log2(1+SNR)
Note:
SNRdB = 10 log10(SNR)
when stated in dB, so be careful about mixing the two logarithmic bases in this problem.
The SNR quantity in the Shannon capacity equation is numerical (not dB) and the logarithm is base 2.
SNR of 10dB is numerically equal to 10
SNRdB = 10dB = 10log10(SNR)
10=10log10(SNR)
1=log10(SNR)
SNR =101= 10

## Slide 47: Exercise
1. | If the SNR of wireless channel 10dB then calculate maximum data rate through channel with bandwidth of 200 KHz. Answer[691.8 kbps]
Given: Bandwidth B=200KHz
SNR=10dB=10log10(SNR)=10
Using Shannon’s formula
C = B * log2(1+SNR)
= 200KHz * log2(1+10)
= (200*103) * log2(1+10)
= 200*103 * 3.45943
= 691.886 * 103
C = 691.89 Kbps
Note:
SNRdB = 10 log10(SNR)
when stated in dB, so be careful about mixing the two logarithmic bases in this problem.
The SNR quantity in the Shannon capacity equation is numerical (not dB) and the logarithm is base 2.
SNR of 10dB is numerically equal to 10
SNRdB = 10dB = 10log10(SNR)
10=10log10(SNR)
1=log10(SNR)
SNR =101= 10

## Slide 48: Classifications of Transmission Media

## Slide 49: Classifications of Transmission Media
Infrared
Micro waves
Radio waves
Transmission Media
Guided
Media
Unguided
Media
Co-axial Cable
Fibre Optics
Twisted Pair
Physical path between transmitter and receiver
Waves are guided along a solid medium
wireless transmission

## Slide 50: General Frequency Ranges
VLF | Very Low Frequency | VHF | Very High Frequency
LF | Low Frequency | UHF | Ultra High Frequency
MF | Medium Frequency | SHF | Super High Frequency
HF | High Frequency | EHF | Extremely High Frequency
Frequency and wavelength are
inversely proportional to each other.

## Slide 51: General Frequency Ranges
Sr. | Band Name | Frequency | Wavelength | Application
1 | Very Low Frequency-VLF | 3–30 kHz | 100–10 km | Navigation, time signals, submarine communication, wireless heart rate monitors, geophysics etc.
2 | Low Frequency-LF | 30–300 kHz | 10–1 km | AM longwave broadcasting (Europe and parts of Asia), RFID, amateur radio
3 | Medium Frequency-MF | 300–3,000 kHz | 1,000–100 m | AM (medium-wave) broadcasts, amateur radio, avalanche beacons
4 | High Frequency-HF | 3–30 MHz | 100–10 m | Shortwave broadcasts, citizens band radio, aviation communications, RFID, radar, marine and mobile radio telephony
5 | Very High Frequency-VHF | 30–300 MHz | 10–1 m | FM, television broadcasts, ground-to-aircraft and aircraft-to-aircraft communications, land mobile and maritime mobile communications, weather radio
6 | Ultra High Frequency-UHF | 300–3,000 MHz | 1–0.1 m | Television broadcasts, microwave oven, radio astronomy, mobile phones, wireless LAN, Bluetooth, ZigBee, GPS, satellite radio, Remote control systems
7 | Super High Frequency-SHF | 3–30 GHz | 100–10 mm | Wireless LAN, most modern radars, communications satellites, cable and satellite television broadcasting
8 | Extremely High Frequency-EHF | 30–300 GHz | 10–1 mm | Microwave remote sensing, directed-energy weapon, millimetre wave scanner, wireless LAN (802.11ad)

## Slide 52: Multiplexing
Definition:
Multiplexing is a technique
used to combine &
send the multiple data streams
over a single medium.
The process of combining the data streams is known as multiplexing &
hardware used for multiplexing is known as a multiplexer.

## Slide 53: Why Multiplexing?
Cost per kbps of transmission facility declines with an increase in the data rate
Cost of transmission and receiving equipment declines with increased data rate
When multiple signals share the common medium, there is a possibility of collision. Multiplexing concept is used to avoid such collision.
The bandwidth of a medium can be utilized effectively.

## Slide 54: Types of Multiplexers
Multiplexers
Analog
Digital
FDM
Frequency Division Multiplexing
TDM
Time Division Multiplexing

## Slide 55: Multiplexing Techniques: Frequency Division Multiplexing (FDM)
Analog technique
FDM is a technique in which the available bandwidth of a single transmission medium is subdivided into several channels.
The pivotal aim of the FDM is to subdivide the available bandwidth into different frequency channels and allocate them to different devices.
FDM is mainly used in radio broadcasts and TV networks.

## Slide 56: Multiplexing Techniques: Time Division Multiplexing (TDM)
Digital technique
In FDM, all signals operate at the same time with different frequency, but in case of TDM, all signals operate at the same frequency with different time.
In TDM, the total time available in the channel is distributed among different users. Therefore, each user is allocated with different time interval known as a Time slot at which data is to be transmitted by the sender.
A user takes control of the channel for a fixed amount of time.
In TDM, data is not transmitted simultaneously rather the data is transmitted one-by-one.
TDM is mainly used in Telephone lines, ISDN (Integrated Services Digital Network) telephone lines.

## Slide 57: Communication Networks

Looping
Topics to be covered
  LANs, MANs and WANs
  Switching Techniques
  Circuit Switching
  Packet Switching
  Circuit Switching vs Packet Switching

## Slide 58: LANs, MANs and WANs
Full-form | Local Area Network | Metropolitan Area Network | Wide Area Network
Propagation delay | Short | Moderate | High
Transmission speed | High comparatively | Average comparatively | Low comparatively
Ownership | Private | Private or public | Private or public
Congestion | Low comparatively | Average comparatively | High comparatively
Maintenance | Easy | Difficult than LAN | Difficult than MAN and LAN
Scope | Small (1 to 10 Km) e.g. Small building, cluster of building, organization | Multiple Building or Society or in a city.(upto 100 Km area) | Multiple city or country (beyone 100Km)
Medium | Cable | Telephone lines | Telephone lines, satellite

## Slide 59: Switching Techniques

## Slide 60: Switching Techniques

## Slide 61: Switching Techniques
For transmission of data beyond a local area, communication is typically achieved by transmitting data from source to destination through a network of intermediate switching nodes.
Purpose is to provide a switching facility that will move the data from node to node until they reach their destination.
The nodes are connected to each other in some topology by transmission links.
Each station attaches to a node, and the collection of nodes is referred to as a communication network.
Two types of Switching Techniques:
  Circuit Switching
  Packet Switching

## Slide 62: Circuit Switching

## Slide 63: Circuit Switching
Connection-oriented networks
Dedicated communication path between two stations
The path is reserved for the single pair of end users
This technique is suitable for long continuous transmission, like voice calls.
E.g. public telephone network

## Slide 64: Packet Switching

## Slide 65: Packet Switching
Connectionless networks
Each node determines next leg of transmission for each packet.
Message is divided and grouped into a number of units called packets that are individually routed from the source to the destination.
This technique guarantees better resource utilization.
E.g. data transfer

## Slide 66: Circuit Switching vs Packet Switching

## Slide 67: Circuit Switching vs Packet Switching
Circuit Switching | Packet Switching
It is a connection oriented network switching technique. | It is a connectionless network switching technique.
Dedicated path has to be established between the source and the destination before transfer of data commences. | There is no need to establish a dedicated path from the source to the destination.
Data packets are routed along the same dedicated path. | Different data packets follow different paths.
Initially designed for voice transfer. | Initially designed for data transfer.
It is not a store and forward transmission. | It is store and forward transmission.
Data is processed and transmitted by the source station only. | Data is processed and transmitted, not only by the source station but at each switching station.
There are 3 phases in circuit switching i) Connection Establishment ii) Data Transfer iii) Connection Released | In Packet switching directly data transfer takes place .

## Slide 68: GTU Questions
Sr. | Question | Marks | Year
1. | Differentiate: Circuit Switching and Packet Switching. | 7 | Win’17,18 Sum’18,19
2. | Explain the Nyquist Theorem. Find the relationship among the following terms: Channel Capacity(C), Bandwidth(B) and Signal-to-Noise Ratio(SNR). | 7 3 | Sum’18 Win’19
3. | Define the term Multiplexing. Explain the FDM and TDM with one example each. | 4 7 | Sum’18 Sum’19
4. | We have a channel with a 1-MHz bandwidth. The SNR value for this channel is 63. What are the appropriate Bit rate and Signal level using Shannon’s and Nyquist’s Formula? | 7 | Win’19
5. | A typical voice channel has SNR as 30dB and Bandwidth as 2.7KHz. Calculate the approximate maximum information capacity of the channel? | 7 | Win’19
6. | Define: Peak Amplitude (A), Frequency (f) and Period (T). | 3 | Win’17
7. | Compare the LAN and WAN. | 3 | Sum’18
8. | What is noise? Discuss briefly types of noise and its effect on transmission signal. | 4 | Win’18
9. | What do you mean by channel capacity? What are the factors that affect it? | 3 | Win’17,18

## Slide 69: References
Book: | Wireless Communications & Networks, Second Edition, William Stallings by Pearson

## Slide 70: Thank You