## Slide 1: Unit-2: Wireless Communication Technology PART-1:Cellular Wireless Networks
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof.Swati R Sharma
Mobile Computing Wireless Communication
(MCWC)
GTU # 3170710

## Slide 2: Cellular Wireless Networks

Looping
Topics to be covered-Cellular Wireless Networks
  Principles of Cellular Networks
  First Generation Analog
  Second-Generation TDMA
  Second-Generation CDMA
  Third-Generation Systems

## Slide 3: Principles of Cellular Networks

## Slide 4: Principles of Cellular Networks
Cellular technology is the foundation of Mobile Wireless Communications.
It support the users in location that are not easily served by wired networks.
Cellular network is an underlying technology for mobile phones, personal communication systems, wireless networking etc.
The technology is developed for mobile radio telephone to replace high power transmitter/receiver systems with low power transmitter/receiver.
Cellular networks use low power, shorter range and more transmitters for data transmission.

## Slide 5: Cellular Network Organization

## Slide 6: Cellular Network Organization
Multiple low power transmitters
  100w or less
Area divided into cells
  Each with own antenna
  Each with own range of frequencies
  Served by Base Station (BS)
    Transmitter, receiver, control unit
  Adjacent cells on different frequencies to avoid crosstalk
Notes: MSC:Mobile Switching Centre

## Slide 7: Shape of Cells
Square
  Width d cell has four neighbours at distance d and four at distance d
  However, this geometry is not ideal
  Better if all adjacent antennas equidistant
    Simplifies choosing and switching to new antenna
Hexagon
  Provides equidistant antennas
  Radius defined as radius of circum-circle
    Distance from center to vertex equals length of side
  Distance between centers of cells radius R is R
  Not always precise hexagons
    Topographical limitations
    Local signal propagation conditions
    Location of antennas

## Slide 8: Frequency Reuse

## Slide 9: Frequency Reuse
Frequency reusing is the concept of using the same radio frequencies within a given area, that are separated by considerable distance, with minimal interference, to establish communication.
Benefits of Frequency Reuse:
  Allows communications within cell on a given frequency
  Limits escaping power to adjacent cells
  Allows re-use of frequencies in nearby cells
  Uses same frequency for multiple conversations

## Slide 10: Frequency Reuse
Example:
N cells all using same number of frequencies
K total number of frequencies used in systems
Each cell has K/N frequencies
Advanced Mobile Phone Service (AMPS)
Given: N=7
K=395 kHz
Find: Frequency of each cell
Solution: Frequency of each cell==
2
3
1
4
5
7
6

## Slide 11: Characterizing Frequency Reuse
D: Minimum distance between centers of cells that use the same band of frequencies (called co-channels)
R: Radius of a cell
d: Distance between centers of adjacent cells (d = R)
N: Number of cells in repetitious pattern
2
3
1
4
5
7
6
5
2
1
D
R
d

## Slide 12: Cluster Size

## Slide 13: Cluster Size
How to find cluster size of cellular network?

## Slide 14: Cluster Size
How to find cluster size of cellular network?
Formula:
N=I2+J2+(I X J)
N: | No. of cell with unique/non repeated frequency
2
3
1
4
5
7
6
5
2
1

## Slide 15: Cluster Size
How to find cluster size of cellular network?
Formula:
Now, if we want to find distance to reach from cell1 to another cell1 then,
Given: I=1,J=2
Solution: N=12+22+(1X2)
=1+4+2
=7
N=I2+J2+(I X J)
N: | No. of cell with unique/non repeated frequency
I: | No. of steps required to move in one direction in order to reach cell with same frequency
J: | No. of steps required to move in other direction(i.e. 60° anticlockwise) in order to reach cell with same frequency.
2
3
1
4
5
7
6
5
2
1
i=1
i=2
j=1
i=1
j=1
j=2

## Slide 16: Exercise: Cluster Size
Find cluster size of cellular network.
Formula:
Now, if we want to find distance to reach from cell1 to another cell1 then,
Given: I=2,J=3
Solution: N=22+32+(2X3)
=4+9+6
N=19
N=I2+J2+(I X J)

## Slide 17: Characterizing Frequency Reuse

## Slide 18: Characterizing Frequency Reuse
Possible values of N are 1, 3, 4, 7, 9, 12, 13, 16, 19, 21, …
For Hexagonal geometry
Therefore,
D: Minimum distance between centers of cells that use the same band of frequencies (called co-channels)
R: Radius of a cell
d: Distance between centers of adjacent cells (d = R)
N: Number of cells in repetitious pattern
2
3
1
4
5
7
6
5
2
1
D
R
d

## Slide 19: Increasing Capacity

## Slide 20: Increasing Capacity
As the demand for wireless service increases, the number of channels assigned to a cell eventually becomes insufficient to support the required number of users.
At this point, cellular design techniques are needed to provide more channels per unit coverage area.
Techniques such as
  Cell splitting
  Cell Sectoring
  Coverage zone approaches
  are used in practice to expand the capacity of cellular systems.

## Slide 21: Cell Splitting

## Slide 22: Cell Splitting
Cell splitting is the process of subdividing a congested cell into smaller cells
  Each with its own base station and a corresponding reduction in antenna height and transmitter power.
Cell splitting increases the capacity of a cellular system since it increases the number of times that channels are reused.
By defining new cells which have a smaller radius than the original cells and by installing these smaller cells (called microcells) between the existing cells.
  Capacity increases due to the additional number of channels per unit area.
The original cell size is about 6.5 to 13km.
To split the cell in smaller cells, the power level must be reduced to keep the signal within cell.
  Ideally 1.5Km cells are close to practical minimum size.

## Slide 23: Cell Sectoring

## Slide 24: Cell Sectoring
One way to increase to subscriber capacity of a cellular network is replace the omni-directional antenna at each base station by three (or six) sector antennas of 120 (or 60) degrees opening.
Each sector can be considered as a new cell, with its own (set of) frequency channel(s).
2
3
1
4
5
7
6
5
2
1
Sector-1
Sector-2
Sector-n

## Slide 25: Cell Sectoring
One way to increase to subscriber capacity of a cellular network is replace the omni-directional antenna at each base station by three (or six) sector antennas of 120 (or 60) degrees opening.
Each sector can be considered as a new cell, with its own (set of) frequency channel(s).
Sectorization is less expensive than cell-splitting, as it does not require the acquisition of new base station sites
60º
120º

## Slide 26: Cell Splitting vs Cell Sectoring
Cell Splitting | Cell Sectoring
Here large macro-cell are dedicated to high-speed traffic. Therefore number of handoffs will be reduced. | Decreases the coverage area of a group of channels and increases the number of handoffs.
Cell are divided into smaller cells each with own base station and reduced frequency. | Cell are sectored into angle of either 60 or 120 degree.
May lead to co-channel interference | Decrease in co-channel interference
Radius of the cell is decreased | Radius of the cell is kept constant

## Slide 27: Operation of Cellular Systems

## Slide 28: Operation of Cellular Systems
Base Station: A base station is a fixed point of communication for cellular phones on a carrier network.
  The most important part of the cellular network is the base station.
It contain 3 elements
  Antenna- handles ranging of signals
  Controller- handles call process between mobile and network.
  Transceivers- transmit and receives signals

## Slide 29: Operation of Cellular Systems
Each Base station is connected to a MTSO (Mobile Telecommunication Switching Office).
MTSO is also connected with PTSN (Public Telecommunications Switching Network).
MTSO
Connects calls between mobile units and from mobile to fixed telecommunications network
Assigns voice channel
Performs handoffs
Monitors calls (billing)

## Slide 30: Cellular System
The Cellular System is fully automated except placing or answering the call.
Two types of channel available between
Base Station
Mobile Unit
Control Channel
Traffic Channel
Contains information for setting up and maintaining calls, establish relationship between mobile unit and nearest Base Station
Carry voice or data connections between users.

## Slide 31: Typical Call in Single MTSO Area
Mobile unit initialization
  When mobile is turns ON,
  Scan and select strongest set up control channel
  Automatically selected BS antenna of cell
    Usually but not always nearest (propagation anomalies)
  Handshake between MTSO and Mobile unit via base station(BS) to identify user and register location
  Scan repeated to allow for movement
    Change of cell
  Mobile unit monitors for pages

## Slide 32: Typical Call in Single MTSO Area
Mobile originated call
  Check set up channel is free
    Monitor forward channel (from BS) and wait for idle
  Send number on pre-selected channel
  The BS will send request to MTSO
Paging
  MTSO attempts to connect to mobile unit
  Paging message sent to BSs depending on called mobile number
  Paging signal transmitted on set up channel

## Slide 33: Typical Call in Single MTSO Area
Call accepted
  Mobile unit recognizes number on set up channel
  Responds to BS which sends response to MTSO
  MTSO sets up circuit between calling and called BSs
  MTSO selects available traffic channel within cells and notifies BSs
  BSs notify mobile unit of channel
Ongoing call
  Voice/data exchanged through respective BSs and MTSO

## Slide 34: Typical Call in Single MTSO Area
Handoff
  Mobile unit moves out of range of cell into range of another cell
  Traffic channel changes to one assigned to new BS
    Without interruption of service to user

## Slide 35: Call in Single MTSO Area: Other Functions
Call blocking
  During mobile-initiated call stage, if all traffic channels busy, mobile tries again
  After number of fails, busy tone is returned
Call termination
  User hangs up
  MTSO informed
  Traffic channels at two BSs released
Call drop
  BS cannot maintain required signal strength
  Traffic channel dropped and MTSO informed
Calls to/from fixed and remote mobile subscriber
  MTSO connects to PSTN
  MTSO can connect mobile user and fixed subscriber via PSTN
  MTSO can connect to remote MTSO via PSTN or via dedicated lines
  Can connect mobile user in its area and remote mobile user

## Slide 36: Mobile Radio Propagation Effects

## Slide 37: Mobile Radio Propagation Effects
Signal strength
  Strength of signal between BS and mobile unit strong enough to maintain signal quality at the receiver
  Not strong enough to create too much cochannel interference
  Noise varies
    Automobile ignition noise greater in city than in suburbs
    Other signal sources vary
    Signal strength varies as function of distance from BS
    Signal strength varies dynamically as mobile unit moves

## Slide 38: Mobile Radio Propagation Effects
Reflection:
  Propagation wave impinges on an object which is large as compared to wavelength
  May have phase shift from original
  May cancel out original or increase it
  E.g. surface of the Earth, buildings, walls, etc.
Diffraction
  Radio path between transmitter and receiver obstructed by surface with sharp irregular edges
  Waves bend around the obstacle, even when LOS (line of sight) does not exist
Scattering
  Objects smaller than the wavelength of the propagation wave
  e.g. foliage, street signs, lamp posts

## Slide 39: Mobile Radio Propagation Effects
Fading
  In wireless communication signal fading occurs due to
  Time variation of received signal
  Caused by changes in transmission path(s)
  Atmospheric conditions (rain)
  Movement of (mobile unit) antenna
Multipath effect
  It means signal travels from source may take multiple path to reach destination.
  The signals receives at then receiver end is sum of all multipath signals.
  It may leads to phase difference due to comparatively longer and shorter path of traversal in multipath effect.

## Slide 40: Types of Fading

## Slide 41: Types of Fading
Fast fading
  Rapid changes in strength over distances about half wavelength
Slow fading
  Slower changes due to user passing different height buildings, gaps in buildings etc.
  Over longer distances than fast fading
Flat fading
  Nonselective
  Affects all frequencies in same proportion
Selective fading
  Different frequency components affected differently

## Slide 43: First Generation Analog

## Slide 44: First Generation Analog
Refers to 1G (first generation of wireless cellular technology mobile telecommunications)
Uses analog radio signals
Provides basic voice service
Nippon Telephone and Telegraph (NTT) in Tokyo started the first commercial analog cellular system in December 1979
Transmission speed was very low (1-2Kbps).
Each phone contained
  32-bit serial number
  10 digit phone number in its PROM
The pivotal idea behind 1G Cellular network was that the geographical area is divided among cells
  Each cell served by base station

## Slide 45: First Generation Analog: Call Sequence
Subscriber initiates call by keying in number and presses send
MTSO validates telephone number and checks user authorized to place call
  Some service providers require a PIN to counter theft
MTSO issues message to user's phone indicating traffic channels to use
MTSO sends ringing signal to called party
  All operations, 2 through 4, occur within 10s of initiating call
When called party answers, MTSO establishes circuit and initiates billing information
When one party hangs up MTSO releases circuit, frees radio channels, and completes billing information

## Slide 46: First Generation Analog
Features
  Channel Bandwidth: 30kHz
  Data transmission rate: 1-2kbps
  No. of control channel: 42
  No. of voice channel: 790
  Cell radius: 2-20km
  Modulation-voice channel: FM (Frequency Modulation)
  Modulation-control channel: FSK
  Circuit switching
Limitations
  Limited capacity:1-2kbps
  Lack of privacy- No encryption
  Poor sound quality
  No room for spectrum growth
  Unreliable hand-off
  No internet

## Slide 47: Second Generation -2G
TDMA & CDMA

## Slide 48: Second-Generation
Second Generation TDMA
(Time Division Multiple Access)
Second Generation CDMA
(Code Division Multiple Access)

## Slide 49: FDMA, TDMA, CDMA

## Slide 51: Second-Generation TDMA
It is a digital cellular telephone communication technology.
It facilitates many users to share the same frequency without interference.
TDMA technology divides a signal into various timeslots, and increases the data carrying capacity.
TDMA is used in digital mobile radio systems.
The individual mobile stations cyclically assign a frequency for the exclusive use of a time interval.

## Slide 52: Second-Generation TDMA: Advantages and Disadvantages
Advantages
  Flexible rates (i.e. several slots can be assigned to a user, for example, each time interval translates 32Kbps, a user is assigned two 64 Kbps slots per frame).
  Can withstand with variable bit rate traffic.
  Number of slots allocated to a user can be changed frame by frame (for example, two slots in the frame 1, three slots in the frame 2, one slot in the frame 3).
  No guard band required for the wideband system.
  No narrowband filter required for the wideband system.
Disadvantages
  High data rates of broadband systems require complex equalization.
  Call time is needed in each slot to accommodate time to inaccuracies (due to clock instability).
  Electronics operating at high bit rates increase energy consumption.
  Complex signal processing is required to synchronize within short slots.

## Slide 53: Second-Generation CDMA
In CDMA, each group of users is given a shared code.
Many codes occupy the same channel, but only those users associated with a particular code can communicate.
Every channel uses the full available spectrum.
Each conversations are encoded with a pseudo-random digital sequence and then transmitted using a wide frequency range.
Provides better voice quality and data communication.
Digital traffic channels
  Support digital data
  Voice traffic digitized
  User traffic (data or digitized voice) converted to analog signal for transmission
Encryption
  Simple to encrypt digital traffic
Error detection and correction
More capacity than TDMA

## Slide 54: Second-Generation CDMA: Advantages and Disadvantages
Advantages
  It does not require any synchronization
  It has a very high spectral capacity, thus many numbers of users can share in the same bandwidth
  CDMA channel is not easily decode-able
  Dropouts occur only when the phone is at least twice as far from the base station.
  High voice quality as well as signal quality
  Flexible allocation of resources
  Operate at a very low power level
Disadvantages
  Does not provide international roaming capabilities like GSM.
  Information related to CDMA is stored in phone memory rather than SIM memory like GSM, thus, tedious to upgrade Mobile unit.
  Limited handset, because at present the major mobile companies use GSM technology.
  Performance degrades with an increase in the number of users

## Slide 55: Second-Generation
Features
  Emits comparatively less radio power
  Maximum power drawn by mobile unit is 20Watts
  Encryption facility
  Error detection and correction
  Internet was provided
Limitations
  Difficult to handle complex data such as Video
  Higher signal strength is required to make device work

## Slide 56: Third Generation -3G

## Slide 57: Third-Generation Systems
Introduced in year 2000
Used WCDMA (Wideband CDMA) technology
Support circuit and packet switching
Objective is to provide fairly high-speed wireless communications to support
  Multimedia data
  Video
  Voice
  Web browsing
  TV streaming
  Video conferencing
  Navigation
  Email
More coverage with lowest investment

## Slide 58: Third-Generation Systems
Features
  Technology used: WCDMA/CDMA
  Bandwidth: 5-10 Mbps
  Frequency Band:15-25 GHz
  User circuit and packet switching
  Higher Security
Limitations
  Cost of mobile unit is higher
  Cost of 3G license services is higher.

## Slide 59: GSM vs CDMA

## Slide 60: GSM vs CDMA
GSM | CDMA
Global System for Mobile communication | Code Division Multiple Access
Technology: FDMA & TDMA | CDMA
Data rate: 42Mbps in HSPA (3G) | Data rate: 3.6Mbps in CDMA
GSM supports transmitting data and voice together | CDMA doesn’t support it
Here customer information is stored in SIM card. | Here customer information is stored in Handset.
Global market share is 75% | Global market share is 25%
SIM specific. User can use/upgrade to multiple handset | Handset specific
Security is comparatively lower than CDMA | Provides more security as encryption is inherit feature
Support International roaming | CDMA doesn’t support this facility

## Slide 61: Comparison of Mobile Generations

## Slide 62: Comparison of Mobile Generations
Parameters | 1G | 2G | 3G | 4G | 5G
Introduced in | 1980’s | 1990’s | 2000’s | 2010’s | 2020’s
Bandwidth | 2kbps | 64kbps | 2Mbps | 200Mbps | 1Gbps
Standard- Technology | AMPS-analog NMT-Nordic Mobile Telephone | TDMA,CDMA(2G) EDGE,GPRS(2.5G) GSM-digital cellular | 3G,HSPA,HSPA+ WCDMA-broadband UMTS | 4G,LTE Standard-Unified IP | Single Unified Standard-Unified IP Seamless
Switching Technique | Circuit Switching | Circuit Switching & Packet Switching | Packet Switching | Packet Switching | Packet Switching
Multiplexing Technique | FDMA | TDMA/CDMA | CDMA | CDMA | CDMA
Core Network | PSTN | PSTN | Packet Network | Internet | Internet
Features | Mobility, voice call | Roaming Voice quality SMS,MMS | Global Roaming, High speed data Internet(limited) | Internet, MobileIP, Wi-Max | Internet <1 msec latency IoT
Handoff | Horizontal | Horizontal | Horizontal | Horizontal & Vertical | Horizontal & Vertical

## Slide 63: GTU Questions: Unit 2-Part 1
Sr. | Question | Marks | Year
1. | Describe Cell Splitting and Cell Sectoring with its limitations in detail. | 7 | Win’19
2. | Justify, Why Hexagon cell shape is used in cellular network? | 3 | Win’20
3. | Define following.1) Fading 2) Modulation | 3 | Win’18
4. | Define Reflection, Refraction and diffraction. | 4 | Sum’19

## Slide 64: References
Book: | Wireless Communications & Networks, Second Edition, William Stallings by Pearson

## Slide 65: Thank You