## Slide 1: Unit-2: Wireless Communication Technology PART-4 : Coding and Error Control
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof.Swati R Sharma
Mobile Computing and Wireless Communication (MCWC)
GTU # 3170710

## Slide 2: Coding and Error Control

Looping
Topics to be covered- Coding and Error Control
  Error Detection
  Block Error Correction Codes
  Convolutional Codes
  Automatic Repeat Request

## Slide 3: Coding and Error Control
For reliable communication, errors must be detected and corrected.
A situation in which received information doesn’t match with the sender’s information.
At the time of transmission a digital signal may suffer from noise, that introduces errors in the data.
It means a 0 bit may change to 1 or a 1 bit may change to 0.
Data-link layer uses some error control mechanism to ensure that frames (data bit streams) are transmitted with certain level of accuracy.
Need to understand how errors is controlled and to know what types of errors may occur.
Error detection and correction are implemented either at the data link layer or the transport layer of the OSI model.

## Slide 4: Coding and Error Control
Regardless of the design of the transmission system, there will be errors, resulting in the change of one or bits in a transmitted frame.
Three approaches are used to deal with data transmission errors:
  Error detection codes
    Detects the presence of an error
  Automatic repeat request (ARQ) protocols
    Receiver discards a block of data in which an error is detected
    Transmitter retransmits that block of data
  Error correction codes, or forward correction codes (FEC)
  Designed to detect and correct errors
  Avoiding the need for retransmission because retransmission is highly inefficient and error rates may be high.

## Slide 5: Types of Errors

## Slide 6: Types of Errors
In a frame, there is only one bit, anywhere though, which is corrupt.
Frame is received with more than one bits in corrupted state.
Frame contains more than1 consecutive bits corrupted.

## Slide 7: Error Detection

## Slide 8: Error Detection
0101110011
1000010111
1000000011
1111110000
0110011001
When a message is transmitted, it may get scrambled due to noise or data may get corrupted.
To avoid this, we use error-detecting codes that are additional data added to a given digital message to help us detect if an error occurred during transmission of the message.
E.g. parity check

## Slide 9: Error Detection Process
Transmitter
  For a given frame, an error-detecting code (check bits) is calculated from data bits
  Check bits are appended to data bits
Receiver
  Separates incoming frame into data bits and check bits
  Calculates check bits from received data bits
  Compares calculated check bits against received check bits
  Detected error if mismatch occurs
Transmitter
Receiver
01100011

## Slide 10: Error Detection Techniques

## Slide 11: Error Detection Techniques
Error Detection Techniques
Parity Check
Cyclic Redundancy Check (CRC)
Checksum

## Slide 12: Parity Check

## Slide 13: Parity Check
A parity check is the process that ensures accurate data transmission between nodes during communication.
A parity bit is appended to the original data bits
Parity Check
Even Parity Check
no. of "1 bits" in the entire word is even.
Odd Parity Check
no. of "1 bits" in the entire word is odd.

## Slide 14: Error Detection in Parity check
Parity checking at the receiver can be detected by the presence of an error if the parity of the receiver signal is different from the expected parity.
It means, if it is known that the parity of the transmitted signal is always going to be "even" and if the received signal has an odd parity, then the receiver can conclude that the received signal is not correct.
If an error is detected, then the receiver will ignore the received byte and request for retransmission of the same byte to the transmitter.
Drawback of parity check
If two (or any even number of bits are inverted due to errors), an undetected error occurs.
Transmission Medium

## Slide 15: Error Detection Techniques
Error Detection Techniques
Parity Check
Cyclic Redundancy Check
Checksum

## Slide 16: Cyclic Redundancy Check

## Slide 17: Cyclic Redundancy Check
CRC or Cyclic Redundancy Check is a method of detecting accidental changes/errors in the communication channel.
CRC is based on binary division.
In CRC, a sequence of redundant bits, called cyclic redundancy check bits, are appended to the end of data unit so that the resulting data unit becomes exactly divisible by a second, predetermined binary number.
At the destination, the incoming data unit is divided by the same number. If at this step there is no remainder(zero remainder), the data unit is assumed to be correct and is therefore accepted.
A non-zero remainder indicates that the data unit has been damaged in transit and therefore must be rejected.

## Slide 18: Cyclic Redundancy Check: Example (Transmitter)
1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0
10101
1
1 | 0 | 1 | 0 | 1
⊕
0
1
1
1
0
0
1
⊕
0
1
0
0
1
⊕
1
1
1 | 0 | 1 | 0 | 1
0
0
1
1
0
⊕
0 | 0 | 0 | 0 | 0
0
0
1
1
0
0
1 | 0 | 1 | 0 | 1
0
0
1
⊕
1 | 0 | 1 | 0 | 1
1
0
1
1
0
0
⊕
1
1 | 0 | 1 | 0 | 1
1
1
1
1
0
0
1
⊕
1 | 0 | 1 | 0 | 1
1
0
1
0
1
Remainder (CRC)= 1011
Now, at the receiver end, Remainder = 1011 is appended to Data=1101101
Therefore, Transmitter will send Data=11011011011
Given: Data=1101101
Divisor=10101
Dividend (data+n-bit(0)) = 11011010000
n-bit->appending ‘0’-bit n times, where n is 1-bit less than divisor

## Slide 19: Cyclic Redundancy Check: Example (Receiver)
Dividend
Divisor
Quotient
Remainder
Generator Polynomial
Content of frame
Used for calculating checksum
Not used

## Slide 20: Cyclic Redundancy Check: Example (Receiver)
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
10101
1
1 | 0 | 1 | 0 | 1
⊕
0
1
1
1
0
0
1
⊕
0
1
0
0
1
⊕
1
1
1 | 0 | 1 | 0 | 1
0
0
1
1
0
⊕
0 | 0 | 0 | 0 | 0
1
0
1
1
0
1
1 | 0 | 1 | 0 | 1
0
0
1
⊕
1 | 0 | 1 | 0 | 1
1
1
1
1
0
1
⊕
1
1 | 0 | 1 | 0 | 1
0
1
0
1
0
1
1
⊕
1 | 0 | 1 | 0 | 1
0
0
0
0
0
Remainder = 00000
Given: Data Received= 11011011011
Divisor=10101

## Slide 21: Cyclic Redundancy Check: Error Example (Receiver)
1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1
10101
1
1 | 0 | 1 | 0 | 1
⊕
0
1
1
1
0
0
1
⊕
0
1
0
0
1
⊕
0
1
1 | 0 | 1 | 0 | 1
0
0
1
1
1
⊕
0 | 0 | 0 | 0 | 0
1
0
1
1
1
1
1 | 0 | 1 | 0 | 1
0
0
1
⊕
1 | 0 | 1 | 0 | 1
1
1
0
1
0
1
⊕
1
1 | 0 | 1 | 0 | 1
0
1
0
0
0
1
0
⊕
0 | 0 | 0 | 0 | 0
0
1
0
0
1
Remainder = 0101 (which is non-zero)
Given: Data Received= 11011011011
Data Received= 11011001011
Divisor=10101

## Slide 22: Cyclic Redundancy Check : Flowchart

## Slide 23: Cyclic Redundancy Check : Digital Logic CRC

## Slide 24: Cyclic Redundancy Check: Exercise
Given: Data=1010000
Divisor=1001
Dividend (data+n-bit(0)) = 1010000000
n-bit->appending ‘0’-bit n times, where n is 1-bit less than divisor
ANS: CRC=011

## Slide 25: Error Detection Techniques
Error Detection Techniques
Parity Check
Cyclic Redundancy Check
Checksum

## Slide 26: Checksum
For error detection by checksums, data is divided into fixed sized frames or segments(k-segments).
For each k-segments, it contains m-bits
For E.g:There are 11001100, 10101010, 11110000 and 11000011 data, so 4 frames/segments, therefore
  k=4
  m=8
Sender | Receiver
Step-1:Segments are added using 1’s complement arithmetic to get the sum. Step-2:Sum is complemented to get the checksum. Step-3:Checksum segment is sent along with the data segments.
Step-1:All received segments are added using 1’s complement arithmetic to get complemented sum. Step-2:If the result is zero, the received data is accepted; otherwise discarded.

## Slide 27: Checksum: Example
Given frames, where k=4 and m=8
Frame 1 | 11001100
Frame 2 | 10101010
Frame 3 | 11110000
Frame 4 | 11000011
Sender | Receiver
Frame 1: 1 1 0 0 1 1 0 0 Frame 2: 1 0 1 0 1 0 1 0 Ans:
+
0
1
1
0
1
1
1
1
0
1
+
1
1
1
1
0
1
1
1
0
Frame 3:
+
1 1 1 1 0 0 0 0
1
1
1
0
0
1
1
0
1
1
1
1
Add carry-bit
+
1
0
0
0
1
0
1
1
0
1
1
1
Frame 4:
+
1 1 0 0 0 0 1 1
1
1
0
1
0
1
0
0
1
1
Add carry-bit
+
1
0
0
1
1
0
1
0
0
1
1
Checksum
1’s compliment
1 1 0 1 0 0 1 1
Frame 1: 1 1 0 0 1 1 0 0 Frame 2: 1 0 1 0 1 0 1 0 Ans: Add carry-bit
+
0
1
1
0
1
1
1
1
0
1
+
1
1
1
1
0
1
1
1
0
Frame 3:
+
1 1 1 1 0 0 0 0
1
1
1
0
0
1
1
0
1
1
1
1
Add carry-bit
+
1
0
0
0
1
0
1
1
0
1
1
1
Frame 4:
+
1 1 0 0 0 0 1 1
1
1
0
1
0
1
0
0
1
1
Add carry-bit
+
1
0
0
1
1
0
1
0
0
1
1
Checksum
1 1 0 1 0 0 1 1
+
1 1 1 1 1 1 1 1
1’s compliment
0 0 0 0 0 0 0 0
Accept Data
Add carry-bit

## Slide 28: Checksum: Example with Error
Given frames, where k=4 and m=8
Frame 1 | 11001100
Frame 2 | 10101010
Frame 3 | 11110000
Frame 4 | 11000011
Sender | Receiver
Frame 1: 1 1 0 0 1 1 0 0 Frame 2: 1 0 1 0 1 0 1 0 Ans: Add carry-bit
+
0
1
1
0
1
1
1
1
0
1
+
1
1
1
1
0
1
1
1
0
Frame 3:
+
1 1 1 1 0 0 0 0
1
1
1
0
0
1
1
0
1
1
1
1
Add carry-bit
+
1
0
0
0
1
0
1
1
0
1
1
1
Frame 4:
+
1 1 0 0 0 0 1 1
1
1
0
1
0
1
0
0
1
1
Add carry-bit
+
1
0
0
1
1
0
1
0
0
1
1
Checksum
1’s compliment
1 1 0 1 0 0 1 1
Frame 1: 1 1 0 0 1 1 0 0 Frame 2: 1 0 1 0 1 0 1 0 Ans: Add carry-bit
+
0
1
1
0
1
1
1
1
0
1
+
1
1
1
1
0
1
1
1
0
Frame 3:
+
1 1 1 1 0 0 0 0
1
1
1
0
0
1
1
0
1
1
1
1
Add carry-bit
+
1
0
0
0
1
0
1
1
0
1
1
1
Frame 4:
+
1 1 0 0 0 0 1 1
1
1
0
1
0
1
0
0
1
1
Add carry-bit
+
1
0
0
1
1
0
1
0
0
1
1
Checksum
1 1 0 1 0 0 0 1
+
1 1 1 1 1 1 0 1
1’s compliment
0 0 0 0 0 0 1 0
Reject Data

## Slide 29: Checksum: Exercise
Frame 1 | 10011001
Frame 2 | 11100010
Frame 3 | 00100100
Frame 4 | 10000100
Sum: 00100101
Checksum: 11011010

## Slide 30: Wireless Transmission Errors
Error detection requires retransmission
Detection inadequate for wireless applications
Error rate on wireless link can be high, results in a large number of retransmissions
Long propagation delay compared to transmission time
Therefore, for wireless transmission, error detection scheme is inadequate.

## Slide 31: Block Error Correction Codes: FEC process
Transmitter
  Forward error correction (FEC) encoder maps each k-bit block into an n-bit block codeword
  Codeword is transmitted; analog for wireless transmission
Receiver
  Incoming signal is demodulated
  Block passed through an FEC decoder
FEC decoder: Possible outcomes
  A: No errors present, i.e. codeword matches with original codeword
  B: Decoder detects and corrects bit errors
  C: Decoder detects but cannot correct bit errors; reports uncorrectable error
  D: Decoder detects no bit errors, though errors are present

## Slide 32: Block Error Correction Codes
Error Detection
and Correction
codes
FEC
(Forward Error Correction)
BEC
(Backward Error Correction)
Block Error Codes
Convolution Codes
ARQ
(Automatic Repeat Request)
Hamming Code
Cyclic Code
BCH Code
Reed Solomon Code
Block Interleaving

## Slide 33: Hamming Code
Hamming code is a block code that is capable of detecting up to two simultaneous bit errors and correcting single-bit errors.
It was developed by R.W. Hamming for error correction.
In this coding method, the source encodes the message by inserting redundant bits within the message.
These redundant bits are extra bits that are generated and inserted at specific positions in the message itself to enable error detection and correction.
When the destination receives this message, it performs recalculations to detect errors and find the bit position that has error.

## Slide 34: Hamming Code: Encoding a message
Step 1 − Calculation of the number of redundant bits.
Step 2 − Positioning the redundant bits.
Step 3 − Calculating the values of each redundant bit.

## Slide 35: Hamming Code Example: Encoding
Data: m=1011001(7-bit)
The number of redundant bits can be calculated by: 2r ≥ m + r + 1
where, r = redundant bit, m = data bit
Step-1: Calculate value of redundant bit(r)
Formula: 2r ≥ m+r+1
2r ≥ 7+r+1
Assuming r=3: 23 ≥ 7+3+1
8 ≥ 11
Assuming r=4: 24 ≥ 7+4+1
16 ≥ 12
Therefore, r=4
Step-3:
X

## Slide 36: Hamming Code Example
Data: m=1011001(7-bit)
Step-2: Positioning the redundant bits
  The r redundant bits placed at bit positions of powers of 2, i.e. 1, 2, 4, 8, 16 etc.
  They are referred in the rest of this text as r1 (at position 1), r2 (at position 2), r3 (at position 4), r4 (at position 8) and so on.
  Data-bit+ redundant-bit= 7-bit+4-bit=11-bit
  Redundant bits= r1, r2, r4, r8
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
r1
r2
r4
r8
1
0
1
1
0
0
1

## Slide 37: Hamming Code Example
Step-3: Calculating the values of each redundant bit
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
r1
r2
r4
r8
1
0
1
1
0
0
1
r1 | 1,3,5,7,9,11
r2 | 2,3,6,7,10,11
r4 | 4,5,6,7
r8 | 8,9,10,11
This example consider ‘EVEN PARITY’ bit

## Slide 38: Hamming Code Example
Step-3: Calculating the values of each redundant bit
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
r1
r2
r4
r8
1
0
1
1
0
0
1
r1 | 1,3,5,7,9,11
r2 | 2,3,6,7,10,11
r4 | 4,5,6,7
r8 | 8,9,10,11
11
1
9
1
7
1
5
0
3
1
r1
0
Even
Parity
Value of r1=
11
1
10
0
7
1
6
0
3
1
r2
1
Odd
Parity
Value of r2=
7
1
6
0
5
0
r4
1
Odd
Parity
Value of r4=
11
1
10
0
9
1
R8
0
Even
Parity
Value of r8=
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
1
0
1
1
0
0
1
1
0
1
0

## Slide 39: Hamming Code Example: Decoding
Step-4: decoding
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
1
0
1
1
0
0
1
1
0
1
0
11
1
9
1
7
1
5
0
3
1
1
0
Even
Parity
r1=
0
11
1
10
0
7
1
6
0
3
1
2
1
Even
Parity
r2=
0
r1 | 1,3,5,7,9,11
r2 | 2,3,6,7,10,11
r4 | 4,5,6,7
r8 | 8,9,10,11
7
1
6
0
5
0
4
1
Even
Parity
r4=
0
11
1
10
0
9
1
8
0
Even
Parity
r8=
0
No Error

## Slide 40: Hamming Code Example: Decoding (Error)
Step-4: decoding
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
1
0
1
0
1
0
1
1
0
1
0
11
1
9
1
7
1
5
0
3
1
1
0
Even
Parity
r1=
0
11
1
10
0
7
1
6
1
3
1
2
1
Odd
Parity
r2=
1
r1 | 1,3,5,7,9,11
r2 | 2,3,6,7,10,11
r4 | 4,5,6,7
r8 | 8,9,10,11
7
1
6
1
5
0
4
1
Odd
Parity
r4=
1
11
1
10
0
9
1
8
0
Even
Parity
r8=
0
Value=0110=>6(binary)
Error detected in bit 6
Error will be corrected after changing bit 6 from ‘1’ to ‘0’

## Slide 41: Hamming Code Example: Decoding (Error)
Step-4: decoding
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
1
0
1
0
0
0
1
1
0
1
0
11
1
9
1
7
0
5
0
3
1
1
0
Odd
Parity
r1=
1
11
1
10
0
7
0
6
0
3
1
2
1
Odd
Parity
r2=
1
r1 | 1,3,5,7,9,11
r2 | 2,3,6,7,10,11
r4 | 4,5,6,7
r8 | 8,9,10,11
7
0
6
0
5
0
4
1
Odd
Parity
r4=
1
11
1
10
0
9
1
8
0
Even
Parity
r8=
0
Value=0111=>7(binary)
Error detected in bit 7
Error will be corrected after changing bit 7 from ‘1’ to ‘0’

## Slide 42: Hamming Code Example: Exercise
1
0
0
1
1
0
1
1
0
0
1
1
0
1
1
1
0
0
1
1
0
1
0
1
1
0
0
1
1
0
0
1
0
1
1
0
0
1
1
1
0
0
1
0
Data: 1 0 0 1 1 0 1
1
Data: 1 0 0 1 1 1 0 0 1 0 1
Data
Adding r1
Adding r2
Adding r4
Adding r8

## Slide 43: Hamming Code Example: Exercise
Error in transmission:
Error bit Detection
1
0
0
1
1
1
0
0
1
0
1
1
0
0
1
0
1
0
0
1
0
1
Sent
Error
Received
1
0
0
1
0
1
0
0
1
0
1
11
10
9
8
7
6
5
4
3
2
1
1
0
0
1
0
1
0
0
1
0
1
11
10
9
8
7
6
5
4
3
2
1
1
0
0
1
0
1
0
0
1
0
1
11
10
9
8
7
6
5
4
3
2
1
1
0
0
1
0
1
0
0
1
0
1
11
10
9
8
7
6
5
4
3
2
1
7
The bit in position 7 is in error
0
1
1
1

## Slide 44: Block Error Correction Codes
Error Detection
and Correction
codes
FEC
(Forward Error Correction)
BEC
(Backward Error Correction)
Block Error Codes
Convolution Codes
ARQ
(Automatic Repeat Request)
Hamming Code
Cyclic Code
BCH Code
Reed Solomon Code
Block Interleaving

## Slide 45: Cyclic Code
The cyclic property of code words is that any cyclic-shift of a code word is also a codeword.
Cyclic codes follow this cyclic property
For a linear code C, if every code word i.e., C = C1,C2,......Cn from C has a cyclic right shift of components, it becomes a code word.
This shift of right is equal to n-1 cyclic left shifts. Hence, it is invariant under any shift.
So, the linear code C, as it is invariant under any shift, can be called as a Cyclic code.
Cyclic codes are used for error correction.
They are used to correct double errors and burst errors.

## Slide 46: Cyclic Code
There are two important property of cyclic code
Property of Linearity
Property of Shifting

## Slide 47: Cyclic Code: Example 1
Data = { 0000, 0110, 1001, 1111 }
Rule for Linearity:
  A⊕B=C⊕D
  A⊕C=B⊕D
  B⊕C=A⊕D
A
B
C
D
 | 0 | 0 | 0 | 0
⊕ | 0 | 1 | 1 | 0
 | 0 | 1 | 1 | 0
A⊕B
 | 1 | 0 | 0 | 1
⊕ | 1 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
C⊕D
=
 | 0 | 0 | 0 | 0
⊕ | 1 | 0 | 0 | 1
 | 1 | 0 | 0 | 1
A⊕C
 | 0 | 1 | 1 | 0
⊕ | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 1
B⊕D
=
 | 0 | 1 | 1 | 0
⊕ | 1 | 0 | 0 | 1
 | 1 | 1 | 1 | 1
B⊕C
 | 0 | 0 | 0 | 0
⊕ | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 1
A⊕D
=
Therefore, the Code is Linear

## Slide 48: Cyclic Code: Example 1
Data = { 0000, 0110, 1001, 1111 }
Rule for Shifting: Cyclic right shifts
  Right-shift A
A
B
C
D
0 | 0 | 0 | 0
0 | 0 | 0 | 0
= A
0 | 0 | 0 | 0
= A
0 | 1 | 1 | 0
0 | 0 | 1 | 1
=X
  Right-shift B
1 | 0 | 0 | 1
1 | 1 | 0 | 0
= X
1 | 1 | 1 | 1
1 | 1 | 1 | 1
= D
1 | 1 | 1 | 1
=D
  Right-shift D
  Right-shift C
This code doesn’t follows one of the rule:
Rule for Linearity √
Rule for Shifting X
Therefore, this is NOT cyclic code

## Slide 49: Cyclic Code: Example 2
Data = { 0000, 0101, 1010, 1111 }
Rule for Linearity:
  A⊕B=C⊕D
  A⊕C=B⊕D
  B⊕C=A⊕D
A
B
C
D
 | 0 | 0 | 0 | 0
⊕ | 0 | 1 | 0 | 1
 | 0 | 1 | 0 | 1
A⊕B
 | 1 | 0 | 1 | 0
⊕ | 1 | 1 | 1 | 1
 | 0 | 1 | 0 | 1
C⊕D
=
 | 0 | 0 | 0 | 0
⊕ | 1 | 0 | 1 | 0
 | 1 | 0 | 1 | 0
A⊕C
 | 0 | 1 | 0 | 1
⊕ | 1 | 1 | 1 | 1
 | 1 | 0 | 1 | 0
B⊕D
=
 | 0 | 1 | 0 | 1
⊕ | 1 | 0 | 1 | 0
 | 1 | 1 | 1 | 1
B⊕C
 | 0 | 0 | 0 | 0
⊕ | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 1
A⊕D
=
Therefore, the Code is Linear

## Slide 50: Cyclic Code: Example 2
Data = { 0000, 0101, 1010, 1111 }
Rule for Shifting:
  Right-shift A
A
B
C
D
0 | 0 | 0 | 0
0 | 0 | 0 | 0
= A
0 | 0 | 0 | 0
= A
0 | 1 | 0 | 1
1 | 0 | 1 | 0
= C
0 | 1 | 0 | 1
=B
1 | 0 | 1 | 0
= C
  Right-shift B
1 | 0 | 1 | 0
0 | 1 | 0 | 1
= B
1 | 0 | 1 | 0
= C
0 | 1 | 0 | 1
= B
1 | 1 | 1 | 1
1 | 1 | 1 | 1
= D
1 | 1 | 1 | 1
=D
  Right-shift D
  Right-shift C
This code follows both:
Rule for Linearity
Rule for Shifting
Therefore, this is cyclic code

## Slide 51: Cyclic Code: Example 2(wrong example)
Data Sent = { 0000, 0101, 1010, 1111 } Data Received = { 0001, 0101, 1010, 1111 }
Rule for Linearity:
  A⊕B=C⊕D
  A⊕C=B⊕D
  B⊕C=A⊕D
A
B
C
D
 | 0 | 0 | 0 | 1
⊕ | 0 | 1 | 0 | 1
 | 0 | 1 | 0 | 0
A⊕B
 | 1 | 0 | 1 | 0
⊕ | 1 | 1 | 1 | 1
 | 0 | 1 | 0 | 1
C⊕D
≠
 | 0 | 0 | 0 | 1
⊕ | 1 | 0 | 1 | 0
 | 1 | 0 | 1 | 1
A⊕C
 | 0 | 1 | 0 | 1
⊕ | 1 | 1 | 1 | 1
 | 1 | 0 | 1 | 0
B⊕D
≠
 | 0 | 1 | 0 | 1
⊕ | 1 | 0 | 1 | 0
 | 1 | 1 | 1 | 1
B⊕C
 | 0 | 0 | 0 | 1
⊕ | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 0
A⊕D
≠
Therefore, the Code is NOT Linear

## Slide 52: Cyclic Code: Example 2
Data = { 0000, 0101, 1010, 1111 } Data Received = { 0001, 0101, 1010, 1111 }
Rule for Shifting:
  Right-shift A
A
B
C
D
0 | 0 | 0 | 1
1 | 0 | 0 | 0
= X
0 | 1 | 0 | 0
= X
0 | 1 | 0 | 1
1 | 0 | 1 | 0
= C
0 | 1 | 0 | 1
=B
1 | 0 | 1 | 0
= C
  Right-shift B
1 | 0 | 1 | 0
0 | 1 | 0 | 1
= B
1 | 0 | 1 | 0
= C
0 | 1 | 0 | 1
= B
1 | 1 | 1 | 1
1 | 1 | 1 | 1
= D
1 | 1 | 1 | 1
=D
  Right-shift D
  Right-shift C
Therefore, from both the property we can conclude that
Error is present in Block -A

## Slide 53: Features of Cyclic code
The cyclic codes have a very good performance in detecting
  single-bit errors
  double errors
  odd number of errors
  burst errors
They can easily be implemented in hardware and software.
They are especially fast when implemented in hardware.

## Slide 54: Block Error Correction Codes
Error Detection
and Correction
codes
FEC
(Forward Error Correction)
BEC
(Backward Error Correction)
Block Error Codes
Convolution Codes
ARQ
(Automatic Repeat Request)
Hamming Code
Cyclic Code
BCH Code
Reed Solomon Code
Block Interleaving

## Slide 55: BCH Codes

## Slide 56: BCH Codes
BCH codes are named after the inventors Bose, Chaudari and Hocquenghem.
Subset of cyclic code
During the BCH code design, there is control on the number of symbols to be corrected and hence multiple bit correction is possible.
BCH codes is a powerful technique in error correcting codes.
For any positive integers m ≥ 3 and t < 2m-1 there exists a BCH binary code.
Following are the parameters of BCH code:
  Block length n = 2m-1 (where m is any positive integer and m ≥ 3)
  Number of message bits: k ≥ n-mt (t is no. of bits a BCH code can detect and correct error)
  Minimum distance dmin ≥ 2t + 1
  This code can be called as t-error-correcting BCH code

## Slide 57: BCH Codes
Polynomial P(X)
X3+X+1
X4+X+1
X8+X7+X6+X4+1
X10+X8+X5+X4+X2+X+1
X5+X2+1
X10+X9+X8+X6+X5+X3+1
The central idea is to compute an error-locator polynomial and solve for its roots.
The complexity of the algorithm increases only as the square of the number of errors to be corrected.

## Slide 58: Reed-Solomon Codes

## Slide 59: Reed-Solomon Codes
Reed - Solomon error correcting codes are one of the oldest codes that were introduced in 1960s by Irving S. Reed and Gustave Solomon
Reed-Solomon (RS) codes are a widely used subclass of non-binary BCH codes
With RS codes, data are processed in chunks of m bits, called symbols
An (n, k), RS (Reed-Solomon Codes) code has the following parameters:
Thus, the encoding algorithm expands a block of k symbols to n symbols by adding n - k redundant check symbols.
Typically, m is a power of 2; a popular value of m is 8
Symbol length: | m bits per symbol
Block length: | n = 2m – 1 [symbols = m(2m – 1) bits]
Data length: | k symbols
Size of check code: | n – k = 2t [symbols = m(2t) bits]
Minimum distance: | dmin = 2t + 1 symbols

## Slide 60: Reed-Solomon Codes
A Reed - Solomon encoder accepts a block of data and adds redundant bits (parity bits) before transmitting it over noisy channels.
On receiving the data, a decoder corrects the error depending upon the code characteristics.

## Slide 61: Reed-Solomon Codes
Given: t=1
m=2
K=4
Denoting the symbol as 0,1,2,3 we can write their binary equivalents as
0->00
1->01
2->10
3->11
The code has following parameters:
n = 2m-1 = 22 - 1 = 3 Symbols = 6 bits
(n-k) = 2 Symbols = 4 bits
Therefore, this code can correct any burst error that spans a symbol of 2 bits.

## Slide 62: Reed-Solomon Codes: Application
Storage areas like CDs, DVDs, Blu-ray Discs
High speed data transmission technologies such as DSL and WiMAX
High speed modems
QR Codes
Broadcast systems such as satellite communications
Storage systems such as RAID 6

## Slide 63: Block Interleaving

## Slide 64: Block Interleaving
Interleaving is a tool that is used to enhance existing error correcting codes so that they can be used to perform burst error correction
Most error correcting codes (ECCs) are designed to correct random errors, i.e. error caused by additive noise that is independent of each other.
Burst error are the errors that occur in a sequence or as groups.
They are caused due to defects in storage media or disruption in communication signals due to external factors like lightning etc.
Interleaving modifies the ECC or does some processing on the data after they are encoded by ECCss as well.

## Slide 65: Block Interleaving Process
In Block Interleaving Process, the message is ordered in a repeating sequence of bytes.
The interleaver accepts data symbols in blocks and performs identical permutations on the blocks before transmitting them.
For example, the sequential blocks of code may be written to a matrix in a row-wise manner and then read out from the matrix in a column-wise manner. This method is known as Periodic Interleaving

## Slide 66: Block Interleaving: Example

## Slide 67: Block Error Correction Codes
Error Detection
and Correction
codes
FEC
(Forward Error Correction)
BEC
(Backward Error Correction)
Block Error Codes
Convolution Codes
ARQ
(Automatic Repeat Request)
Hamming Code
Cyclic Code
BCH Code
Reed Solomon Code
Block Interleaving

## Slide 68: Convolutional Codes

## Slide 69: Convolutional Codes
The convolutional coding has been one of the most widely used error corrections in digital wireless communication.
Generates redundant bits continuously
Error checking and correcting carried out continuously
If data are transmitted and received in a more or less continuous stream, a block code, particularly one with a large value of n, may not be as convenient as a code that generates redundant bits continuously so that error checking and correcting are carried out continuously.

## Slide 70: Convolutional Codes
In block codes, the data comprises of a block of data of a definite length.
However, in convolutional codes, the input data bits are not divided into block but are instead fed as streams of data bits, which convolve to output bits based upon the logic function of the encoder.
Unlike block codes, where the output codeword is dependent only on the present inputs, whileT in convolutional codes, output stream depends not only the present input bits but also only previous input bits stored in memory.

## Slide 71: Convolutional Codes: Example
(n,k,K)=(n,4,3), where k=1101
A convolutional code is specified by three parameters
  k: message bits
  n: codeword bits
  K: Constraint length
Don’t send message bits, send only parity bits
Use a sliding window to select which message bits may participate in the parity calculations

## Slide 72: Convolutional Codes: Example 1
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
Don’ t send message bits, send only parity bits
k=1011
K=3(encoder memory)
Find n(codeword)

## Slide 73: Convolutional Codes: Example 1
1 | 0 | 1 | 1
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
k=
m2
m1
m0
X1=m0 ⊕ m1 ⊕ m2
X2=m0 ⊕ m2
Time | Input | Shift register |  |  | Output | 
 |  | m0 | m1 | m2 | X1 | X2
-1 | - | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 |  | 
1 | 0 | 0 | 1 | 0 |  | 
1
1
1
0
2 | 1 | 1 | 0 | 1 |  | 
0
0
3 | 1 | 1 | 1 | 0 |  | 
0
1
4 | 0 | 0 | 1 | 1 |  | 
0
1
5 | 0 | 0 | 0 | 1 |  | 
1
1
n= |  |  |  |  |  |  |  |  |  |  |  | 
1
1
1
0
0
0
0
1
0
1
1
1

## Slide 74: Convolutional Codes: Example 1 state diagram
Time | Input | Shift register |  |  | Output | 
 |  | m0 | m1 | m2 | X1 | X2
-1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 |  | 
1 | 0 | 0 | 1 | 0 |  | 
1
1
1
0
2 | 1 | 1 | 0 | 1 |  | 
0
0
3 | 1 | 1 | 1 | 0 |  | 
0
1
4 | 0 | 0 | 1 | 1 |  | 
0
1
5 | 0 | 0 | 0 | 1 |  | 
1
1
Input | Previous State | Next State
0 | 00 | 
a= | 00
b= | 10
c= | 01
d= | 11
1 | 00 | 
0 | 10 | 
1 | 10 | 
0 | 01 | 
1 | 01 | 
0 | 11 | 
1 | 11 | 
11
01
00
--
11
01
00
10
a=00
b=10
c=01
d=11
Input 1: | ---------->
Input 0: | 

## Slide 75: Automatic Repeat Request (ARQ)

## Slide 76: Automatic Repeat Request (ARQ)
ARQ Mechanism used in data link control and transport protocols
Automatic Repeat ReQuest (ARQ) is a group of error control protocols for transmission of data over noisy or unreliable communication network.
They are named so because they provide for automatic retransmission of frames that are corrupted or lost during transmission.
ARQ is also known as Positive Acknowledgement with Retransmission (PAR)

## Slide 77: Automatic Repeat Request (ARQ)
Application
  ARQ is often used in Global System for Mobile (GSM) communication
  Shortwave radio to ensure reliable delivery of signals.
  Transmission Control Protocol (TCP)
  Error-correction of message signals in ATM networks.
  High-Level Data Link protocol.
  IBM Binary synchronous Communications Protocol.
  Modem file transfer protocol.
Notes: Search Results
Web results
Asynchronous transfer mode

## Slide 78: Automatic Repeat Request (ARQ): Working
In ARQ protocol, receiver will send an acknowledgement to sender as soon it receives the frame correctly.
If the sender don’t receive the acknowledgement before timeout, then the sender understand that the frame has been lost/corrupted during transmission.
Thus, sender will retransmits the frame.
This process will continue until the frame is transmitted successfully.

## Slide 79: Automatic Repeat Request (ARQ): Types
ARQ Protocols
Stop-and-wait
ARQ
Go-back-N
ARQ
Selective Repeat
ARQ

## Slide 80: Stop-and-wait ARQ
Stop – and – wait ARQ provides unidirectional data transmission with flow control and error control mechanisms, appropriate for noisy channels.
The sender keeps a copy of the sent frame.
It then waits for a finite time to receive a positive acknowledgement from receiver.
If the timer expires, the frame is retransmitted.
If a positive acknowledgement is received then the next frame is sent.

## Slide 81: Go-back-N ARQ
Go – Back – N ARQ provides for sending multiple frames before receiving the acknowledgement for the first frame.
It uses the concept of sliding window, and so is also called sliding window protocol.
The frames are sequentially numbered and a finite number of frames are sent.
If the acknowledgement of a frame is not received within timeout period, all frames starting from that frame are retransmitted.

## Slide 82: Selective Repeat ARQ
Selective Repeat ARQ also provides for sending multiple frames before receiving the acknowledgement for the first frame.
However, here only the erroneous or lost frames are retransmitted, while the good frames are received and buffered.

## Slide 83: GTU Questions: Unit 2-Part 4
Sr. | Question | Marks | Year
1. | Describe Error Control Coding in brief. | 4 | Win’18
2. | How Error Control is implemented using Automatic Repeat Request (ARQ) mechanism? | 7 | Win’19
3. | Enlist and explain Error detection methods in cellular wireless network. | 4 7 | Sum’19 Win’20

## Slide 84: References
Book: | Wireless Communications & Networks, Second Edition, William Stallings by Pearson

## Slide 85: Thank You