## Slide 1: Unit-3: Multiple access in Wireless System
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof.Swati R Sharma
Mobile Computing Wireless Communication
(MCWC)
GTU # 3170710
PART-1 : Multiple access in Wireless System & GSM

## Slide 2: Multiple access in Wireless System & GSM

Looping
Topics to be covered
  Multiple access in Wireless System
  Global system for mobile communication
  GSM architecture
  GSM entities
  Call routing in GSM
  PLMN interface
  GSM addresses and identifiers
  Network aspects in GSM
  GSM frequency allocation
  Authentication and security

## Slide 3: Multiple access in Wireless System

## Slide 4
Multiple access in Wireless System

## Slide 5: Global System for Mobile communication(GSM)

## Slide 6: GSM vs CDMA
GSM | CDMA
Global System for Mobile communication | Code Division Multiple Access
Technology: FDMA & TDMA | CDMA
Data rate: 42Mbps in HSPA (3G) | Data rate: 3.6Mbps in CDMA
GSM supports transmitting data and voice together | CDMA doesn’t support it
Here customer information is stored in SIM card. | Here customer information is stored in Handset.
Global market share is 75% | Global market share is 25%
SIM specific. User can use/upgrade to multiple handset | Handset specific
Security is comparatively lower than CDMA | Provides more security as encryption is inherit feature
Support International roaming | CDMA doesn’t support this facility

## Slide 7: What is GSM?
GSM (Global System for Mobile communications) is an open, digital cellular technology used for transmitting mobile voice and data services.
The concept of GSM emerged from a cell-based mobile radio system at Bell Laboratories in the early 1970s.
The use of harmonised spectrum across most of the globe, combined with GSM’s international roaming capability, allows travellers to access the same mobile services at home and abroad.
GSM enables individuals to be reached via the same mobile number in up to 219 countries.
Notes: GLONASS: GLObal NAvigation Satellite System

## Slide 8: Introduction to GSM
GSM is combination of TDMA (Time Division Multiple Access), FDMA (Frequency Division Multiple Access) and Frequency hopping.
GSM makes use of narrowband Time Division Multiple Access (TDMA) technique for transmitting signals.
GSM was developed using digital technology.
It has an ability to carry 64 kbps to 120 Mbps of data rates.
Presently GSM supports more than one billion mobile subscribers in more than 210 countries throughout the world.
Roaming is the ability to use your GSM phone number in another GSM network.
GSM owns a market share of more than 75% of the world's digital cellular subscribers.

## Slide 9: Introduction to GSM
In GSM, geographical area is divided into hexagonal cells whose side depends upon power of transmitter and load on transmitter (number of end user).
At the centre of cell, there is a base station consisting of a transceiver (combination of transmitter and receiver) and an antenna.

## Slide 10: Why GSM?
Improved spectrum efficiency
International roaming
Low-cost mobile sets and base stations (BSs)
High-quality speech
Compatibility with Integrated Services Digital Network (ISDN) and other telephone company services
Support for new services
Ability to support handheld terminals
ISDN compatibility

## Slide 11: History of GSM
Year | Event
1982 | Group of Special Mobile (GSM) established
1987 | Essential elements of wireless transmission specified
1989 | GSM becomes an ETSI technical committee
1990 | Phase 1 GSM 900 specification (designed 1987 through 1990) frozen
1991 | First GSM network launched
1993 | First roaming agreement came into effect
1994 | Data transmission capability launched
1995 | Phase 2 launched, Fax and SMS roaming services offered
2002 | SMS volume crosses 24 billion/year, 750 million subscribers
Notes: ETSI:European Telecommunications Standards Institute

## Slide 12: GSM Architecture

## Slide 13: GSM Architecture
AUC | Authentication center
BSC | Base station controller
BTS | Base trans-receiver system
EIR | Equipment Identity Register
GMSC | Gateway MSC
HLR | Home Location Register
ISDN | Integrated System Digital Network
MS | Mobile station
MSC | Mobile Switching Centre
PDN | Packet Data Network
PSTN | Public Switching Telephone Network
VLR | Visitor Location Register

## Slide 14: GSM Architecture
MSC
GMSC
ISC
OMC
BSC
BSC
BTS
BTS
BTS
VLR
HLR
AUC
EIR
PSTN
ISDN
PDN
PLMN & INTERNET
Operation &
Maintenance
Centre

## Slide 15: GSM Architecture: Mobile Station (MS)
MS consists of following two components
Mobile Equipment (ME)
Mobile Subscriber Identity Module (SIM)
  Removable plastic card
  Stores Network Specific Data such as list of carrier frequencies and current LAI.
  Stores International Mobile Subscriber Identity (IMSI) + ISDN
  Stores Personal Identification Number (PIN) & Authentication Keys.
  Also stores short messages, charging information, telephone book etc.
Allows separation of user mobility from equipment mobility

## Slide 16: Base Transceiver Station (BTS)

## Slide 17: GSM Architecture: Base Transceiver Station (BTS)
One per cell
Consists of high speed transmitter and receiver
Its transmit power decides size of cell
Function of BTS
  Provides two channels
    Signalling and Data Channel
  Performs error protection coding for the radio channel

## Slide 18: GSM Architecture: Base Station Controller (BSC)
Controls multiple BTS
Functions of BSC
  Performs radio resource management
    Assigns and releases frequencies and time slots for all the MSs in its area
    Reallocation of frequencies among cells
    Hand over protocol is executed here
  Time and frequency synchronization signals to BTSs
  Time Delay Measurement and notification of an MS to BTS
  Power Management of BTS and MS

## Slide 19: GSM Architecture: Mobile Switching Centre (MSC)
Switching node of a PLMN(Public Land Mobile Network)
Task of MSC
  Registration
  Authentication
  Location updating
  Handovers
  Call routing
Mobility of subscribers
  Location registration of subscriber
There can be several MSCs in a PLMN

## Slide 20: GSM Architecture: Gateway MSC (GMSC)
Connects mobile network to a fixed network
  Entry point to a PLMN
Usually one per PLMN
Request routing information from the HLR and routes the connection to the local MSC

## Slide 21: GSM Architecture: Home Location Register(HLR)
For all users registered with the network, HLR keeps user profile.
Logically only one HLR per PLMN
Persistent storage of user data
MSCs exchange information with HLR
When MS registers with a new GMSC, the HLR sends the user profile to the new MSC
Includes information like
  Current location of user
  Authentication data
  Service provisioning information
  Power on status

## Slide 22: GSM Architecture: Visitor Location Register (VLR)
VLR is responsible for a group of location areas, typically associated with an MSC
Contains temporary information needed for call control typically copied from HLR.
When subscriber enters a new MSC, VLR associated with that MSC requests user info from corresponding HLR

## Slide 23: GSM Architecture: AUC and EIR
AUC: Authentication Center
  Accessed by HLR to authenticate a user for service
  Contains authentication and encryption keys for subscribers
EIR: Equipment Identity Register
  Allows stolen or fraudulent mobile stations to be identified

## Slide 24: GSM System Hierarchy
Public Land Mobile Network(PLMN)/ GSM Administrative Region
Location Area
BSC
Location Area (LA)
Base Station Controller (BSC)
Cell
MSC Region
Base Station Controller
Cell
Location Area
Mobile Switching Centre (MSC) Region
Administrative Region
Registration, Authentication, location updating, handovers and call routing
One LA consist of many cell groups & each cell group is assigned to one BSC
One BSC can belong to different LA’s

## Slide 25: GSM Entities

## Slide 26: GSM Entities
  Mobile Equipment (ME)
  Subscriber Identity Module (SIM)
Mobile Station (MS)
  Base Transceiver Station (BTS)
  Base Station Controller (BSC)
Base Station Subsystem (BSS)
  Mobile Switching Center (MSC)
  Home Location Register (HLR)
  Visitor Location Register (VLR)
  Equipment Identity Register (EIR)
  Authentication Center (AUC)
Network and Switching Subsystem (NSS)
  Operation and Maintenance Center (OMC)
Operation and Support Subsystem (OSS)

## Slide 27: GSM Entities
MSC
GMSC
ISC
OMC
BSC
BSC
BTS
BTS
BTS
VLR
HLR
AUC
EIR
PSTN
ISDN
PDN
PLMN & INTERNET
BSS
NSS
OSS

## Slide 28: GSM Addresses and Identifiers

## Slide 29: GSM Addresses and Identifiers: IMSI, IMEI, MSISDN
Notes: TMSI-Temporary Mobile Subscriber Identity

## Slide 30: GSM Addresses and Identifiers: IMSI number
IMSI: International Mobile Subscriber Identity
IMSI identifies registered smartphone users
A working SIM card has a valid IMSI
Each IMSI consists of three parts:
Mobile Subscriber Identification Number (MSIN)
  identifies the subscriber in his or her mobile network.
Mobile Country Code (MCC)
  It gets 3 decimal places and identifies the country of mobile device owner.
Mobile Network Code (MNC)
  It identifies your carrier network
MCC
MNC
MSIN
Maximum 15 digit
3 digits
2-3 digits
National MSI
IMSI
10 digits

## Slide 31: GSM Addresses and Identifiers: IMEI number
15-digit number to uniquely identify a mobile phone device.
Every mobile equipment in this world has a unique identifier which is called IMEI.
  IMEI allocated by the equipment manufacturer and registered by the network operator in the Equipment Identity Register (EIR).

## Slide 32: GSM Addresses and Identifiers: MSISDN number
Mobile Subscriber ISDN Number
MSISDN is primary key to the HLR record.
The MSISDN number is the real telephone number as is known to the external world.
  MSISDN number is public information whereas IMSI is private to the operator. IMSI can be multiple such as when a subscriber opts for fax and data.
  IMSI is assigned a total of three numbers: one for the voice call, one for a fax call and another for the data call.
  MSISDN follows the international ISDN (Integrated Systems Data Network) numbering plan.
CC
NDC
SN
3 digits
2-3 digits
MSISDN
Max. 10 digits
Country Code - CC
National Destination Code - NDC
Subscriber Number - SN

## Slide 33: GSM Addresses and Identifiers: Location Area Identity (LAI)
Each LA in a PLMN has own identifier called Location Area Identifier (LAI) which is structured hierarchically and unique.
Example: 502-20-60001
MCC
MNC
LAC
3 digits
2 digits
LAI
1 to 65536
Mobile Country Code - MCC
Mobile Network Code - MNC
Location Area Code - LAC

## Slide 34: GSM Addresses and Identifiers: Mobile Station Roaming Number (MSRN)
When a subscriber is roaming in another network, a temporary ISDN number assigned to the subscriber called MSRN.
  MSRN assigned by the local VLR in charge of the mobile station and follows the structure of MSISDN.

## Slide 35: GSM Addresses and Identifiers
Temporary Mobile Subscriber Identity (TMSI): TMSI is a temporary identifier assigned by the serving VLR used in place of the IMSI for identification and addressing of the mobile station.
  Together with the current location area, a TMSI allows a subscriber to identified uniquely.
Local Mobile Subscriber Identity (LMSI): LMSI assigned by the VLR and stored in the HLR and used as a searching key for faster database access within the VLR.
Cell Identifier: Within an LA, every cell has a unique Cell Identifier (CI) together with an LAI, a cell can be identified uniquely through Global Cell Identity (LAI & CI).

## Slide 36: Call Routing in GSM

## Slide 37
BTS
BTS
BTS
MS
MS
MS
MS
MS
MS
BTS
BTS
BTS
MS
MS
MS
MS
MS
MS
BTS
BTS
BTS
MS
MS
MS
MS
MS
MS
BSC
BSC
BSC
MSC
MSC
GMSC
VLR
HLR
EIR
AUC
VLR
HLR
EIR
AUC
PSTN
Call Routing in GSM

## Slide 38: Call Routing in GSM: Mobile Phone to Public Switched Telephone Network
Mobile phone subscriber will dial a number on PSTN network
To identify the communicating network the MSC will receive the message of a call request through BTS and BSC respectively.
The MSC checks if the MS is authorized to access the destination network. If YES, then Destination MS is activated, else the service will be denied.
MSC will ask the destination BSC to allocate a traffic channel (radio channel + time slot)
The destination BSC will then allocates the traffic channel and pass the information to PSTN telephone.

## Slide 39: Call Routing in GSM: Mobile Phone to Public Switched Telephone Network
The called party answers the call and the conversation takes place
The MS keeps on taking measurements of the radio channels in the present cell and the neighbouring cells and passes the information to the BSC.
The BSC decides if a handover is required.
If so, a new traffic channel is allocated to the mobile station and the handover takes place.
If handover is not required, the mobile station continues to transmit in the same frequency.

## Slide 40
Fixed Subscriber | PSTN/ISDN Exchange | Gateway MSC | Home Location Register | PSTN/ISDN Exchange | MSC/VLR | Mobile Station
MSISDN
MSISDN
MSISDN
IMSI
MSRN
MSRN
MSRN
MSRN
TMSI
Call Routing in GSM
MSISDN: Mobile Subscriber ISDN | IMSI: Iinternational Mobile Subscriber Identity
TMSI: Temporary Mobile Subscriber Identity | MSRN:Mobile Station Roaming Number

## Slide 41: Call Routing: Mobile-originated

## Slide 42: Mobile-originated call
Step-1 | To initiate a call, the MS request for radio resource allocation to the BSS, which mediates further connection to the Mobile Switching Center (MSC). The BSS assigns the MS a channel with a given frequency and time slot.
Step-2 | BSS initiate the connection to the MSC.
Step-3 | Now as MS had connected to the network, the subscriber needs to be authenticated. As IMSI number is stored in MS SIM card, AUC will verify subscriber’s identity. Thus, MS and MSC are now connected. MSC initiates a ciphering procedure which is transmitted to the BTS, which in turn forwards the message to the MS. it will start the ciphered transmission of information, finalizing the encryption procedure.
Step-4 | MSC verifies that the requested service is allowed for the subscriber. This information is available in VLR. Once the VLR confirms the service requested by the originating MS, the MSC starts the call setup.

## Slide 43: Mobile-originated call
Step-5 | MSC allocates a voice channel between the MSC and the BSS. The MSC routes the call to the dialed number. When the call is received in the PSTN, the MSC is notified that the called subscriber is being alerted, at which point the originating MS receives a ring notification.
Step-6 | To disconnect the call by either party, a disconnect message is sent to the MSC, which releases the communication channels created with the PSTN and the BSS

## Slide 44: Call Routing: PSTN-originated

## Slide 45: PSTN-originated call
Step-1 | When a call is placed from the PSTN, the PSTN uses the information in the phone number (country and if available, operator) to locate GMSC leading to the MSC where the subscriber is registered.
Step-2 | GMSC can request information about the subscriber’s core network and current location by interrogating the HLR.
Step-3 | HLR constantly updates locations of the MS stored in the VLRs of the networks the MS visits. In the HLR, the subscriber MSISDN (phone number) is associated with the IMSI number of the SIM card, which was used to authenticate the subscriber in the visited network as they registered. HLR is aware of the visited MSC/VLR of the MS at a given time.
Step-4 | In order for the GMSC to pass the call to the MSC, the HLR asks a temporary roaming phone number(MSRN) from the MSC. (Mobile Station Roaming Number – MSRN).
Notes: Reference:https://yatebts.com/documentation/concepts

## Slide 46: PSTN-originated call
Step-5 | MSRN is sent back from the HLR to the GMSC.
Step-8 | Then BSC, in turn, page the BTSs assigned to them.
Step-6 | GMSC forward the call to the MSC using the assigned MSRN.
Step-7 | MSC pages all the BSCs in the area that it serves.
Step-9 | Called MS responds to the paging from the BTS, asking to establish a radio channel to the BTS.
Step-10 | Response is forwarded to the MSC, which, once notified, authenticates the MS and initiates the ciphering of the call
Step-11 | MSC sends back to the radio network the call confirmation message, the called MS starts to ring.
Step-12 | Then, MSC notifies the GMSC, which notifies the PSTN that the destination number is being alerted.
Notes: Reference:https://yatebts.com/documentation/concepts

## Slide 47: PLMN Interface

## Slide 48: PLMN Interface
MSC
MSC
GMSC
BSC
EIR
HLR
AUC
VLR
VLR
VLR
BTS
BTS
SS#7 Network
&
Leased Line
SP
SP
SP
SP
SP
SP
PSTN
ISD
PDN
Signaling Data
User data

## Slide 49: PLMN Interface
A basic configuration of a GSM network contains a central HLR and a central VLR, where
  HLR contains all security, provisioning and subscriber related information
  VLR stores the location information and other transient data.
MSC needs subscriber parameter for successful call set-up.
Any data related to user call (connection, teardown, etc.) processed with the SS7 protocol for signaling.
For mobile specific signaling, a protocol stack called MAP (Mobile Application Part) used over the SS7 network which does all database transactions and handover/roaming transactions between the MSC.
MSC uses registers known as SP – Signaling Point.

## Slide 50: GSM Handoff

## Slide 51: Handoff
In cellular communications, the terms handover or handoff refers to the process of transferring ongoing call or data connectivity from old Base Station to new Base Station.
When a mobile moves into the different cell while the conversation is in progress then the MSC (Mobile Switching Centre) will transfer the call to a new channel belonging to the new Base Station.
When a mobile user A moves from one cell to another cell then BTS 1 signal strength loses for the mobile User A and the signal strength of BTS 2 increases and thus ongoing calls or data connectivity for mobile user goes on without interrupting.

## Slide 52: Why Handoff?
Two Reasons
When The Radio Signal’s quality and power decreases to necessary scores, the connection deliver to more powerful cell
When the Traffic Capacity approaches to maximum, the connection deliver to less density of traffic cell

## Slide 53: Handoff Types: Soft Handoff vs Hard Handoff
Hard Handoff | Soft Handoff
Break in the connection occurs while switching from one cell to another. | Break in the connection will not occur due to overlapping cells.
The radio links from the mobile station to the existing cell is broken before establishing a link with the next cell. | In soft handoff, at least one of the links is kept when radio links are added and removed to the mobile station.
It is a “break before make” policy. | It is a “make before break” policy.

## Slide 54: Type of Handover/Handoff
Four types of handover in GSM:
MSC
GMSC
ISC
OMC
BSC
BSC
BTS
BTS
BTS
VLR
HLR
AUC
EIR
PSTN
ISDN
PDN
PLMN & INTERNET
1. Intra - Cell Handover
2. Inter-cell handover
3. Inter-BSC handover
4. Inter-MSC handover
MSC

## Slide 55: Handoff Types

## Slide 56: Network Aspects in GSM

## Slide 57: Network aspects in GSM: Signalling Protocol Structure
GSM architecture is a layered model that is designed to allow communications between two different systems.
The lower layers assure the services of the upper-layer protocols.
Each layer passes suitable notifications to ensure the transmitted data has been formatted, transmitted, and received accurately.
CM MM RR
LAPDm
TDMA
RR
LAPDm
TDMA
CM MM BSSMAP
SCCP
MTP
BSSMAP
SCCP
MTP
Mobile Station
BTS
BSC
MSC
Abis
Um
A
GSM
Layer 3
Layer 2
Layer 1

## Slide 58: Network aspects in GSM: Signalling Protocol Structure
GSM signalling protocol is categorized into three general layers:
Layer 1 - physical layer: It uses the channel structures over the air interface.
Layer 2 - The data-link layer: Across the Um interface, the data-link layer is a modified version of the Link access protocol for the D channel (LAP-D) protocol used in ISDN, called Link access protocol on the Dm channel (LAP-Dm). Across the A interface, the Message Transfer Part (MTP), Layer 2 of SS7 is used.
CM MM RR
LAPDm
TDMA
RR
LAPDm
TDMA
CM MM BSSMAP
SCCP
MTP
BSSMAP
SCCP
MTP
Mobile Station
BTS
BSC
MSC
Abis
Um
A
GSM
Layer 3
Layer 2
Layer 1

## Slide 59: Network aspects in GSM: Signalling Protocol Structure
The GSM signalling protocol is categorized into three general layers:
Layer 3 : GSM signalling protocol’s third layer is divided into three sublayers:
  Radio Resource Management (RR): It controls the set-up, maintenance, and termination of radio and fixed channels, including handovers.
  Mobility Management (MM):It manages the location updating and registration procedures as well as security and authentication.
  Connection Management (CM): It handles general call control and manages Supplementary Services and the Short Message Service(SMS).
CM MM RR
LAPDm
TDMA
RR
LAPDm
TDMA
CM MM BSSMAP
SCCP
MTP
BSSMAP
SCCP
MTP
Mobile Station
BTS
BSC
MSC
Abis
Um
A
GSM
Layer 3
Layer 2
Layer 1

## Slide 60: Network aspects in GSM: Signalling Protocol Structure
MS to BTS Protocols
RR layer :
  Manages a link, both radio and fixed, between the MS and the MSC
  Manages the RR-session, the time when a mobile is in a dedicated mode, and the radio channels including the allocation of dedicated channels.
MM layer: Stacked above the RR layer
CM MM RR
LAPDm
TDMA
RR
LAPDm
TDMA
CM MM BSSMAP
SCCP
MTP
BSSMAP
SCCP
MTP
Mobile Station
BTS
BSC
MSC
Abis
Um
A
GSM
Layer 3
Layer 2
Layer 1
  Handles the functions that arise from the mobility of the subscriber
  Authentication and security aspects
  Location management

## Slide 61: Network aspects in GSM: Signalling Protocol Structure
MS Protocols
CM Layer: Call Management(CM) is topmost layer of the GSM protocol stack
  Responsible for Call Control, Supplementary Service Management, and Short Message Service Management.
  Handles call establishment, selection of the type of service (including alternating between services during a call), and call release.
LADPm: Lightweight Authentication and Delegation Protocol
CM MM RR
LAPDm
TDMA
RR
LAPDm
TDMA
CM MM BSSMAP
SCCP
MTP
BSSMAP
SCCP
MTP
Mobile Station
BTS
BSC
MSC
Abis
Um
A
GSM
Layer 3
Layer 2
Layer 1
  LAPDm is a data link layer protocol used in GSM cellular networks.
  forms Layer 2 of Um interface between the BTS and MS

## Slide 62: Network aspects in GSM: Signalling Protocol Structure
Um interface
The Um interface is the air interface of the GSM mobile telephone standard.
It is the interface between the mobile station (MS) and the Base transceiver station (BTS).
It is known as Um because it is the mobile analog to the U interface of ISDN.
Um is defined in the GSM 04.xx and 05.xx series of specifications.
Um can also support GPRS packet-oriented communication.
CM MM RR
LAPDm
TDMA
RR
LAPDm
TDMA
CM MM BSSMAP
SCCP
MTP
BSSMAP
SCCP
MTP
Mobile Station
BTS
BSC
MSC
Abis
Um
A
GSM
Layer 3
Layer 2
Layer 1

## Slide 63: Network aspects in GSM: Signalling Protocol Structure
BSC Protocols: Uses a different set of protocols after receiving the data from BTS.
Abis interface: Used between the BTS and BSC.
  Allows control of the radio equipment and radio frequency allocation in the BTS.
BSSMAP: Base Station System Management Application Part
  Designed for signalling over the A interface
  Supports both connectionless and connection-oriented services provided by the SCCP
  Supports messages sent between the MSC and the BSS, as well as transparent message transfer between the MSC and the MS
CM MM RR
LAPDm
TDMA
RR
LAPDm
TDMA
CM MM BSSMAP
SCCP
MTP
BSSMAP
SCCP
MTP
Mobile Station
BTS
BSC
MSC
Abis
Um
A
GSM
Layer 3
Layer 2
Layer 1

## Slide 64: Network aspects in GSM: Signalling Protocol Structure
BSC Protocols: Uses a different set of protocols after receiving the data from BTS.
SCCP: Signalling Connection Control Part (SSCP) is a network layer protocol
  Provides extended routing, flow control, segmentation, connection-orientation, and error correction facilities in Signaling System 7 (SS7) telecommunications networks.
  SCCP relies on the services of MTP for basic routing and error detection.
MTP: Message Transfer Part
  Part of the Signalling System 7 (SS7) used for communication in Public Switched Telephone Networks (PSTN).
  MTP is responsible for reliable, unduplicated and in-sequence transport of SS7 messages between communication partners.
CM MM RR
LAPDm
TDMA
RR
LAPDm
TDMA
CM MM BSSMAP
SCCP
MTP
BSSMAP
SCCP
MTP
Mobile Station
BTS
BSC
MSC
Abis
Um
A
GSM
Layer 3
Layer 2
Layer 1

## Slide 65: Network aspects in GSM: Signalling Protocol Structure
MSC Protocols
A interface:
  Used to provide communication between the BSS and the MSC.
  The interface carries information to enable the channels, timeslots and the like to be allocated to the mobile equipment's being serviced by the BSSs.
At the MSC, starting from the BSC, the information is mapped across the A interface to the MTP Layers 1 through 3.
Location registers are included in the MSC databases to assist in the role of determining how and whether connections are to be made to roaming users.
CM MM RR
LAPDm
TDMA
RR
LAPDm
TDMA
CM MM BSSMAP
SCCP
MTP
BSSMAP
SCCP
MTP
Mobile Station
BTS
BSC
MSC
Abis
Um
A
GSM
Layer 3
Layer 2
Layer 1

## Slide 66: GSM Frequency Allocation

## Slide 67: GSM Frequency Allocation
Uplink: is a frequency transmission that links mobile handset to base station
Downlink: is a frequency transmission that links base station to mobile handset
There are 4 major GSM frequency bands
  850 MHz
  900 MHz
  1800 MHz
  1900 MHz
Allocation of band
Country | Frequency Band
United States | 850 MHz and 1900 MHz
Rest of the world (Europe, Middle East, Africa, Asia) | 900 MHz and 1800 MHz

## Slide 68: GSM bands in India
Each way the bandwidth for the GSM system is 25 MHz which provides 125 carriers uplink/downlink each having a bandwidth of 200 kHz.
For Uplink: 900 MHz of frequency is allocated.
  Range: 890-915 MHz
For Downlink: 900 MHz of frequency is allocated.
  Range: 935-960 MHz
Notes: 25000000/125=200000=200KHz

## Slide 69: GSM bands :Carrier frequency and TDMA frames
GSM uses a combination of TDMA and FDMA encoding.
  FDMA:124 channels of 200 kHz
  TDMA:Burst
Freq. Carrier: 200 kHz
TDMA: 8 time slots per freq carrier
No. of carriers = 25 MHz / 200 kHz = 125
Max no. of user channels =125 * 8 = 1000
Practically, a guard band of 100 kHz is provided at the upper and lower end of the GSM and only 124 (duplex) channels are implemented.
Considering guard bands = 124 * 8 = 992 channels
Notes: 25000000/125=200000=200KHz

## Slide 70: Authentication and Security
Authentication involves two functional entities:
  SIM card in the mobile phone
  Authentication Center (AUC)
For authentication; different algorithms used:
  MS algorithm A3
  Voice Privacy key algorithm A8
  Strong over-the-air voice privacy algorithm A5
It used for ciphering and deciphering procedure for signaling, voice, and data.
So, signal, voice, data, and SMS within GSM networks ciphered over the wireless radio interface.

## Slide 71: GTU Questions: Unit 3 GSM
Sr. | Question | Marks | Year
1. | Draw and explain GSM architecture. | 7 7 7 | Sum’19 Sum’20 Win’20
2. | Show the use of below GSM Identifiers. i) IMEI ii) IMSI iii) MSISDN iv) MSRN | 3 4 | Win’18 Win’20
3. | Illustrate different scenarios of Roaming and Handoff in GSM with proper Examples. OR Explain GSM call routing. | 7 7 | Sum’19 Win’19
4. | Compare GSM and CDMA technology. | 3 3 | Win’18 Sum’19
5. | Explain functional architecture of GSM system and types of services provided by GSM. | 7 | Win’18
6. | Explain handover process in cellular system. | 4 4 4 | Win’18 Sum’19 Win’20
7. | Explain the purpose of Home Location Register (HLR). List the information which is stored in Home Location Register (HLR). | 4 3 | Win’18 Win’19
8. | Explain Addresses and Identifiers used in GSM with Example. | 4,3 | Win’19,Sum’20

## Slide 72: References
Book: | Mobile Computing Technology, Applications and service creation , Asoke K Telukder, Roopa R Yavagal by TMH
Web: | https://www.gsma.com/

## Slide 73: Thank You