## Slide 1: Unit-3: Multiple access in Wireless System
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof. Swati R Sharma
Mobile Computing Wireless Communication
(MCWC)
GTU # 2170710
PART-3 : Wi-MAX and Mobile IP

## Slide 2: Wireless System Operations Wi-MAX

Looping
Topics to be covered
  Cordless Systems
  Wireless Local Loop
  WiMAX and IEEE 802.16 Broadband
  Wireless Access Standards

## Slide 3: Cordless System

## Slide 4: Cordless System
Cordless system is a general term of cordless telephones and cordless telecommunication systems.
Cord means a wire, so, a cordless system means wireless system.
A cordless telephone is known as a portable telephone and it acts as a standard phone.
A base station communicates with the cordless handset through radio waves, and this usually only works within a limited range like residence or office.
Example: Digital Enhanced Cordless Telecommunications (DECT) Phone

## Slide 5: Wireless Local Loop - WLL

## Slide 6: Wireless Local Loop - WLL
WLL is a system that connects subscribers to the local telephone station wirelessly.
In telephone, a loop is circuit line from subscriber’s phone to line-terminating equipment at the central office.
Implementation of a local loop especially in rural areas used to remain a risk for many operators due to fewer users and increased cost of materials.
So, Wireless local loop (WLL) has introduced which solves most of these problems.
It is also known as fixed wireless systems.

## Slide 7: Advantages of WLL
It eliminates the first mile or last mile construction of the network connection.
No use of conventional copper wires, thus Low cost
Highly secured due to digital encryption techniques used in wireless communication.
Highly scalable as it doesn’t require the installation of more wires for scaling it.

## Slide 8: Features of WLL
Internet connection via modem
Data service
Voice service
Fax service

## Slide 9: WiMAX and IEEE 802.16

## Slide 10: WiMAX and IEEE 802.16
Wireless Broadband known as Wireless Metropolitan Area Network (Wireless MAN) / Wireless Interoperability Microwave Access (WiMAX).
IEEE 802.16 standard released in April 2002.
It offers an alternative to high bandwidth wired access networks like fiber optic, cable modems and DSL.
It provides network access to buildings through exterior antennas communicating with radio base stations.
Networks can be created in just weeks by deploying a small number of base stations on buildings or poles to create high capacity wireless access systems.

## Slide 11: IEEE Standards
IEEE 802.11 | Wireless LAN
IEEE 802.15 | Wireless Personal Area Network(WPAN)
IEEE 802.16 | Broadband Wireless Access (BBWA)
IEEE 802.20 | Mobile Broadband Wireless Access (MBWA)

## Slide 12: Sub-standards of IEEE 802.16
IEEE 802.16.1 - Air interface for 10 to 66 GHz
IEEE 802.16.2 - Coexistence of broadband wireless access systems
IEEE 802.16.3 - Air interface for licensed frequencies, 2 to 11 GHz

## Slide 13: IEEE 802.16
The 802.16a standard for 2-11 GHz is a wireless metropolitan area network (MAN) technology that will provide broadband wireless connectivity to
  Fixed
  Portable
  Nomadic devices (portable electronic devices for information, entertainment, or communication that can be used outside of the vehicle and inside the vehicle)
It can be used to connect 802.11 hot spots to the Internet, provide campus connectivity, and provide a wireless alternative to cable and DSL for last mile broadband access.

## Slide 14: Deployment of WiMax – IEEE 802.16
IEEE 802.16 standards define how wireless traffic will move between subscribers and core networks.
A subscriber sends wireless traffic at speeds ranging from 2M to 155M bits/sec from a fixed antenna on a building.
Residential subscriber
Base Station
Switching Center
Wireless or wired link using 802.16 protocol
The base station receives transmissions from multiple sites and sends traffic over wireless or wired links to a switching center using 802.16 protocol.
The switching center sends traffic to an ISP or public switched telephone network.
ISP

## Slide 15: Mobile IP

Looping
Topics to be covered
  WiFi vs WiMAX
  Mobile IP
  Wireless Application Protocol

## Slide 16: WiFi vs WiMAX

## Slide 17: WiFi vs WiMAX
Features | WiFi | WiMAX
IEEE Standard | IEEE 802.11x | IEEE 802.16
Data Rate | 300 Mbps | 70 Mbps
Transmission Range | 300 meter | 50Km
Transmission Range | 300 meter | 50Km
Application | WiFi is for LAN applications | WiMAX is for MAN applications
QoS | WiFi does not guarantee any Quality of Service (Qos) | WiMax guarantee Quality of Service (Qos)
Application | WiFi is for LAN applications | WiMAX is for MAN applications

## Slide 18: Mobile IP

## Slide 19: Mobile IP
Mobile IP is a communication protocol (created by extending Internet Protocol, IP) that allows the users to move from one network to another with the same IP address.
It ensures that the communication will continue without user’s sessions or connections being dropped.

## Slide 20: Mobile IP Topology

## Slide 21: Mobile IP
The term “Mobile” in Mobile IP signifies that, while a user is connected to applications across the Internet and the user’s point of attachment changes dynamically, all connections are maintained despite the change in underlying network properties.
Similar to the handoff/roaming situation in a cellular network.
Mobile IP allows the mobile node to use two IP addresses called home address and care of address.
The home address is static and known to everybody as the identity of the host.
The care of address changes at each new point of attachment and can be thought of as the mobile node’s location specific address.

## Slide 22
Mobile IP Architecture
Home Network for A
Foreign Network
Internet or other topology or routers and links
Home Agent
Foreign Agent
1
2
3
4
5
Server X
Mobile Node A
Server X wants to transmit an IP datagram to node A.
The home address of A is advertised and known to X.
X does not know whether A is in the home network or somewhere else.
Therefore, X sends the packet to A with A’s home address as the destination IP address in the IP header.
The IP datagram is routed to A’s home network. At the A’s home network, the incoming IP datagram is intercepted by the home agent.
The home agent discovers that A is in a foreign network.
A care of address has been allocated to A by this foreign network and available with the home agent.
The home agent encapsulates the entire datagram inside a new IP datagram, with A’s care of address in the IP header.
This new datagram with the care of address as the destination address is retransmitted by the home agent.
At foreign network, the incoming IP datagram is intercepted by the foreign agent.
The foreign agent is the counterpart of the home agent in the foreign network.
The foreign agent strips off the outer IP header, and delivers the original datagram to A.
A intends to respond to this message and sends traffic to X.
In this example, X is not mobile; therefore X has a fixed IP address.
For routing A’s IP datagram to X, each datagram is sent to some router in the foreign network. Typically, this router is the foreign agent.
A uses X’s IP static address as the destination address in the IP header.
The IP datagram from A to X travels directly across the network, using X’s IP address as the destination address.

## Slide 23: Working of Mobile IP
Discovery - A mobile node uses a discovery procedure to identify prospective home agents and foreign agents.
Registration - A mobile node uses a registration procedure to inform its home agent of its care-of address.
Tunneling - Tunneling procedure is used to forward IP datagrams from a home address to a care of address.

## Slide 24: Working of Mobile IP: Discovery
Discovery - A mobile node uses a discovery procedure to identify prospective home agents and foreign agents.
Agent Discovery
  HA’s and FA’s broadcast their presence on each network to which they are attached
    Beacon messages via ICMP (Internet Control Message Protocol)and RDP (Router Discovery Protocol)
  MN’s listen for advertisement and then initiate registration

## Slide 25: Working of Mobile IP: Registration Process
Registration - A mobile node uses a registration procedure to inform its home agent of its care-of address.

## Slide 26: Working of Mobile IP: Tunneling
Tunneling - Tunneling procedure is used to forward IP datagrams from a home address to a care of address.

## Slide 27: Mobile IP: Features
Enables hosts to stay connected to the Internet regardless of their location
Enables hosts to be tracked without needing to change their IP address
Requires no changes to software of non-mobile hosts/routers
Requires addition of some infrastructure
Has no geographical limitations
Requires no modifications to IP addresses or IP address format
Supports security

## Slide 28: Wireless Application Protocol

## Slide 29: Wireless Application Protocol
WAP is an application communication protocol
It is designed for access to Internet and advanced telephony services from mobile phones
It is a protocol designed for micro-browsers and it enables the access of internet in the mobile devices
WAP uses mark-up language – WML
WAP can be used from variety of 2G and 3G networks
GPRS and 3G are more suited for these applications

## Slide 30: WAP Protocol Stack

## Slide 31: WAP Protocol Stack
Application Layer (WAE)
Session Layer (WSP)
Transaction Layer (WTP)
Security Layer (WTLS)
Transport Layer (WDP)
Other Services and Applications
GSM
IS-136
CDMA
PHS
CDPD
PDC-P
IDEN
FLEX
etc…
Bearers:
Wireless Application Environment
(WAE)
  User agent which is the browser or a client program.
  Wireless Markup Language (WML) which is a lightweight markup language optimized for use in wireless devices.
  WML Script which is a lightweight client side scripting language.
  Wireless Telephony Application: Telephony services and programming interface.
  WAP Push Architecture which allow for mechanisms to allow origin servers to deliver content to the terminal without the terminal requesting for it.
Primary objective of WAE is to provide an interoperable environment to build services in wireless space.
Content is transported using standard protocols in the WWW domain and an optimized HTTP like protocol in the wireless domain.
WAE architecture allows all content and services to be hosted on standard Web Servers when all content is located using WWW standard URLs.
WAE enhances some of the WWW standards to reflect some of the telephony network characteristics.
Unlike HTTP, WSP has been designed by the WAP Forum to provide fast connection suspension and reconnection.
WSP provides a consistent interface between two session services like client and server.
WSP offers both connection-oriented and connectionless service.
It runs on top of a datagram service such as User Datagram Protocol (UDP) and is part of the standard suite of TCP/IP protocols used to provide a simplified protocol suitable for low bandwidth wireless stations.
WTP supports class of transaction service, optional user-to-user reliability, PDU concatenation and asynchronous transaction.
WTLS incorporates security features that are based upon the established Transport Layer Security(TLS) protocol standard.
It provides data integrity, privacy, authentication, denial of service protection.
WDP is transport layer protocol in WAP architecture.
WDP operates above data capable bearer services supported by various network type general transport service.
It allows WAP to be bearer-independent by adapting the transport layer of the underlying bearer.
The WDP presents a consistent data format to the higher layers of the WAP protocol stack.
Wireless Transaction Protocol
(WTP)
Wireless Session Protocol
(WSP)
Wireless Transport Layer Security
(WTLS)
Wireless Datagram Protocol
(WDP)

## Slide 32: Comparing with Internet Model
HTML
HTTP
TLS/SSL
TCP/IP

## Slide 33: WAP Architecture
Web Server
Content
CGI
Scripts
etc.
WML Decks
with WML-Script
WAP Gateway
WML Encoder
WMLScript
Compiler
Protocol Adapters
Client
WML
WML-Script
WTAI
Etc.
HTTP
WSP/WTP

## Slide 34: References
Book: | Mobile Computing Technology, Applications and service creation , Asoke K Telukder, Roopa R Yavagal by TMH
Web: | https://www.electronics-notes.com/

## Slide 35: Unit-3: Multiple access in Wireless System
swati.sharma@darshan.ac.in
(O) 9727747317
Computer Engineering Department
Prof.Swati R Sharma
Mobile Computing Wireless Communication
(MCWC)
GTU # 2170710
PART-3 : Wi-MAX and Mobile IP